## Slide 1: Graphics Hardware
Sanaa Jeehan
November 9th, 2020
6th Week

## Slide 2: Vector Display
Also called random, stroke, calligraphic displays
Draw object by electron beam, beam can move in any direction

## Slide 3: Vector Display
Early computer displays: basically an oscilloscope –Control X,Y with vertical/horizontal plate voltage
Often used intensity as Z
Refresh Buffer stores plotting commands
  So Frame Buffer often called "Display File”
  provides DPU with needed endpoint coordinates
  Pixel size independent of frame buffer, provides very high resolution

## Slide 4: Advantages of Vector Display
High resolution (good for detailed line drawings)
Crisp lines (no "jaggies")
High contrast (beam can dwell on a single point for some time ==> very bright)
Selective erase (remove commands from display file)
Animation (change line endpoints slightly after each refresh)

## Slide 5: Disadvantages of Vector Display
Complex drawings can have flicker
  Many lines
    so if time to draw > refresh time ==> flicker
High cost--very fast deflection system needed
Hard to get colors
No area fill
  so it’s difficult to use for realistic (shaded) images
1960s Technology, only used for special purpose stuff today

## Slide 6: Raster Display
The screen is divided into lines, and each lines has many dots. The beam scans each line, the beam intensity is creased at a light dot
  Raster: A rectangular array of points or dots
  Scan line: A row of pixels
  Resolution: number of pixels per scan line times the number of scan lines e.g. 640 X 480, 1024 X 768
  Each Pixel on screen visited during each scan
    Scan rate must be >= 30Hz to avoid flicker

## Slide 7: Raster Display
Simplest system: one bit per pixel
  frame buffer called a bitmap
Gray Scale: N bits/pixel
  2^N intensities possible
  memory intensive
  Example:1000 X 1000 X 256 shades of gray ==> 8 Mbits

## Slide 8: Advantages of Raster Display
Low cost (TV technology)
Area fill (entire screen painted on each scan)
Colors
Selective erase (just change contents of frame buffer)
Bright display, good contrast
  but not as good as vector scan can be:
  can’t make beam dwell on a pixel

## Slide 9: Disadvantages of Raster Display
Large memory requirement for high resolution
  (but cost of VRAM has decreased a lot!)
Aliasing (due to finite size of frame buffer)
  Finite pixel size
  Jagged lines (staircase effect)
  Moire patterns, scintillation, "creep" in animations
Raster scan is the principal “now” technology for graphics displays!

## Slide 10: Tektronix Direct View Storage Tube
1st "inexpensive" graphics display device
Extension of vector scan technique
Two electron guns
  writing gun
  flood gun

## Slide 11: Tektronix Direct View Storage Tube
Writing gun beam knocks electrons out leaves + charges behind (constitute image)
Flood gun supplies continuous source of unfocused electrons
  migrate toward the + charges on grid
  pass through grid and strike screen phosphors
    lighted dots
  electrons continue to hit + charges
  continuous light (Up to an hour)

## Slide 12: Erasing a DVST Image
TWO Options
Plus charge applied to entire grid
  Attracts electrons to entire grid
  Entire screen flashes (Image gone)
Minus charge applied to entire grid
  Provides electrons that can be knocked out by writing gun
  Ready to draw next image with writing gun

## Slide 13: Advantages of DVST
No refresh needed
  unlimited image complexity possible
High resolution
Crisp lines
Low cost
  no fast refresh circuitry needed

## Slide 14: Disadvantages of DVST
No selective erase
  whole image or nothing
No animation
Low light output
  poor contrast
  must use in subdued light
No color
No area fill

## Slide 15: Interlaced Displays
All even then all odd screen lines scanned
Typically 1/60 second each
  Same image presented twice in 1/30 second
  Image changed at 1/2 non-interlaced frequency
    less demands on image generation system
    can be less expensive
    30 Hz is borderline for flicker
    lower quality image (seeing half the image at a time)

## Slide 16: Colour Display Hardware - Raster
Each pixel composed of 3 phosphors
  Red, green, and blue
  All of them together form the required colour
3 electron guns shoot their beams through a shadow mask
  so beams hit the sensitive phosphors
Intensity of 3 beams determines how bright each phosphor glows
Human eye detects an additive color mix
  e.g., max red, green, & blue perceived as white

## Slide 17: Colour Display Hardware - Raster

## Slide 18: True Colour & High Colour Systems
True color: direct color system with 8 bits per colour (N=8)
  so 2^24 = 16,777,216 different colors possible for each pixel on screen
  More colors than discernable by human eye
High color: direct color system with: Nr=5, Ng=6, Nb=5
  2^16 = 65, 536 different colors possible

## Slide 19: Colour Graphics on a PC
Graphics capabilities depend on display adapter (video card) in the system
Historical development:
  CGA (Color Graphics Adapter)
  EGA (Enhanced Graphics Adapter)
  VGA (Video Graphics Array)
  Many different types of SVGA cards
  Each display adapter can function in many different text and graphics modes
  Backwards compatibility