## Slide 1: Graphics Hardware
Sanaa Jeehan
March 30th, 2020
7th Week

## Slide 2: Colour Display Hardware - Raster
Each pixel composed of 3 phosphors
  glow red, green, and blue
3 electron guns shoot their beams through a shadow mask
  so beams hit the sensitive phosphors
Intensity of 3 beams determines how bright each phosphor glows
Human eye detects an additive color mix
  e.g., max red, green, & blue perceived as white

## Slide 3: Colour Display Hardware - Raster

## Slide 4: Direct Colour System
Frame buffer divided into bit planes
A bit plane contributes one bit to the color of each pixel on the screen
If resolution of the screen is W x H pixels:
  a bit plane is a W x H x 1 bit memory
Bit planes can be organized into 3 sets
  Each called a color channel: (R, G, B)
  Bit planes of a color channel provide the intensity values fed to that channel’s electron gun
A system with N bit planes per color channel:
  2^N red, 2^N green, & 2^N blue shades
  2^3N different colors displayable simultaneously

## Slide 6: True Colour & High Colour Systems
True color: direct color system with: N=8
  so 2^24 = 16,777,216 different colors possible for each pixel on screen
  More colors than discernable by human eye
High color: direct color system with: Nr=5, Ng=6, Nb=5
  2^16 = 65, 536 different colors possible

## Slide 7: Indirect Colour System
Values stored in bit planes are indices into one or more color lookup tables (CLUTs)
  CLUT stores R, G, B intensity values
  # of bit planes determines # of colors displayable simultaneously on screen
  width of CLUTs determines # of possible colors.

## Slide 9: Indirect Colour System
If system has N bit planes per color channel
And each set of bit planes indexes a CLUT of width w,
  Then number of entries in each CLUT = 2N
  We say there are 23N colors displayable chosen from a total of 23w possible colors
  Each set of 23N colors often called a palette
  CLUTs often called palette registers

## Slide 10: Indirect Colour System - Advantages
Wide CLUTs (large w) ==>huge number of possible colors
Modest # of bitplanes (small N) ==> VRAM not excessive in size
Also, number CLUT entries is modest
  So we get lots of possible colors with relatively little memory expense
Fast animation for certain effects
  just change contents of CLUTS

## Slide 11: Indirect Colour System - Disadvantages
Ultimately number of colors on screen at any one time is limited by number of bit planes (N)
  Even if there’s a large number of possible colors (large CLUT w), only a small fraction of them are usable at one time
  So graphics applications must set up CLUTs with values corresponding to most frequently occurring colors in scene
    Different scenes might require different combinations of colors in the CLUTs
Can be slower: 2nd memory access

## Slide 12: Colour Graphics on a PC
Graphics capabilities depend on display adapter (video card) in the system
Historical development:
  CGA (Color Graphics Adapter)
  EGA (Enhanced Graphics Adapter)
  VGA (Video Graphics Array)
  Many different types of SVGA cards
  Each display adapter can function in many different text and graphics modes
  Backwards compatibility

## Slide 13: Questions ???