## Slide 1
CCoommppuutterer FFununddaammenenttaallss:: PPrradadeeeepp KK.. SSiinhnhaa && PPrriititi SSiinhanha
Ref Page Chapter 9: Input-Output Devices Slide 1/58

## Slide 2: Learning Objectives
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
In this chapter you will learn about:
Input/Output (I/O) devices
Commonly used input devices
Commonly used output devices
Other concepts related to I/O devices
148
Slide 2/58

## Slide 3: I/O Devices
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
148
Slide 3/58
Provide means of communication between a computer and outer world
Also known as peripheral devices because they surround the CPU and memory of a computer system
Input devices are used to enter data from the outside world into primary storage
Output devices supply results of processing from primary storage to users

## Slide 4: Role of I/O Devices
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Input data from external world
Results of processing in human acceptable form
Input data coded in internal form
Processed data in internal form
CPU
and Memory
Input Devices
Output Devices
148
Slide 4/58

## Slide 5: Commonly Used Input Devices
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
149
Slide 5/58
Keyboard device
Point-and-draw devices
Data scanning devices
Digitizer
Electronic cards based devices
Speech recognition devices
Vision based devices

## Slide 6: Keyboard Devices
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
149
Slide 6/58
Allow data entry into a computer system by pressing a set of keys (labeled buttons) neatly mounted on a keyboard connected to a computer system
101-keys QWERTY keyboard is most popular

## Slide 7: The Layout of Keys on a QWERTY Keyboard
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Esc
F1
F2
F3
F4
F5
F6
F7
F8
F9
F10
F11
F12
~
`
! |  | @ |  | # | 3 |  | $ |  | % |  | ^ |  | & |  | * |  | ( |  | )
1 | Q | 2 | W |  |  | E | 4 | R | 5 | T | 6 | Y | 7 | U | 8 | I | 9 | O | 0 P
 |  | A |  | S |  |  | D |  | F |  | G |  | H |  | J |  | K |  | L
_
-
+
=
 Backspace
{
[
}
]

Tab 
:
;
“
‘
 Enter
Caps Lock
Z
X
C
V
B
N
M
<
,
>
.
?
/
Shift
Shift
Alt
|
\
Ctrl
Alt
?
/
Ctrl
Print Screen | Scroll Screen | Pause
Insert | Home | Page Up
Delete | End | Page Down




Num Lock | Caps Lock | Scroll Lock
Num Lock |  | / | * | - | 
7 Home |  | 8  | 9 Pg Up | + | 
4  |  | 5 | 6  |  | 
1 End |  | 2  | 3 Pg Dn |  | Enter
 | 0 Ins |  | . Del |  | 
149
Slide 7/58

## Slide 8: Point-and-Draw Devices
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
149
Slide 8/58
Used to rapidly point to and select a graphic icon or menu item from multiple options displayed on the Graphical User Interface (GUI) of a screen
Used to create graphic elements on the screen such as lines, curves, and freehand shapes
Some commonly used point-and-draw devices are:
Mouse
Track ball,
Joy stick
Light pen and Touch screen

## Slide 9: Mouse
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Commonly used in personal computers and workstations
150
Slide 9/58

## Slide 10: Trackball
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Commonly used in laptop (notebook) computers
Ball to be rolled with fingers
Click buttons
151
Slide 10/58

## Slide 11: Joystick
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Commonly used for video games, flight simulators, training simulators, and for controlling industrial robots
Socket
Ball
Click button
Stick
Light indicator
152
Slide 11/58

## Slide 12: Electronic Pen
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
152
Pen-based point-and-draw device
Used to directly point with it on the screen to select menu items or icons or directly draw graphics on the screen
Can write with it on a special pad for direct input of written information to a system
Pressure on tip of a side button is used to cause same action as right-button-click of a mouse

## Slide 13: Touch Screen
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Most simple, intuitive, and easiest to learn of all input devices
Enables users to choose from available options by simply touching with their finger the desired icon or menu item displayed on the screen
Most preferred human-computer interface used in information kiosks (unattended interactive information systems such as automatic teller machine or ATM)

## Slide 14: Data Scanning Devices
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
153
Input devices that enable direct data entry into a computer system from source documents
Eliminate the need to key in text data into the computer
Due to reduced human effort in data entry, they improve data accuracy and also increase the timeliness of the information processed
Demand high quality of input documents
Some data scanning devices are also capable of recognizing marks or characters
Form design and ink specification usually becomes more critical for accuracy

## Slide 15: Image Scanner
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
153
Input device that translates paper documents into an electronic format for storage in a computer
Electronic format of a scanned image is its bit map representation
Stored image can be altered or manipulated with an image-processing software

## Slide 16: Two Common Types of Image Scanners
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
A flat-bed scanner
A hand-held scanner
153

## Slide 17: Flatbed Scanner
Rectangular in shape
Consists of a flat glass surface covered by a Lid(Cover).
A light source beneath the glass surface moves from left to right in order to scan the document.
Documents are placed upside down on the glass surface in order to be scanned by the scanner.
Size is usually 8.5 x 14 inches

## Slide 18: Handheld Scanner
Consists of a set of LED lights closed in a hard casing.
During the scanning process, the lights are focused on the surface.
Handheld scanners are small and less expensive.
Handheld scanner is moved by hand over the document being scanned.
Rely on the user’s movement to move across the paper.
Handheld Scanner

## Slide 19: Optical CharacterRecognition (OCR) Device
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Scanner equipped with a character recognition software (called OCR software) that converts the bit map images of characters to equivalent ASCII codes
Enables word processing of input text and also requires less storage for storing the document as text rather than an image
OCR software is extremely complex because it is difficult to make a computer recognize an unlimited number of typefaces and fonts
Two standard OCR fonts are OCR-A (American standard) and OCR-B (European standard)

## Slide 20: Optical Mark Reader (OMR)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
155
Scanner capable of recognizing a pre-specified type of mark by pencil or pen
Very useful for grading tests with objective type questions, or for any input data that is of a choice or selection nature
Technique used for recognition of marks involves focusing a light on the page being scanned and detecting the reflected light pattern from the marks
Optical Mark Reader

## Slide 21: Sample Use of OMR
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
For each question, four options are given out of which only one is correct. Choose the correct option and mark your choice against the corresponding question number in the given answer sheet by darkening the corresponding circle with a lead pencil.
The binary equivalent of decimal 4 is: a) 101
b) 111
c) 001
d) 100
The full form of CPU is:
  Cursor Positioning Unit
  Central Power Unit
  Central Processing Unit
  None of the above
Which is the largest unit of storage among the following:
  Terabyte
  Kilobyte
  Megabyte
  Gigabyte
(a) Question sheet
A sample use of OMR for grading tests with objective type questions
(b) Pre-printed answer sheet
1. |  |  |  |  | 
 | a | b | c | d | 
2. |  |  |  |  | 
 | a | b | c | d | 
3. |  |  |  |  | 
 | a | b | c | d | 
Indicates direction in which the sheet should be fed to the OMR
155

## Slide 22: Bar-code Reader
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
155
Scanner used for reading (decoding) bar-coded data
Bar codes represent alphanumeric data by a combination of adjacent vertical lines (bars) by varying their width and the spacing between them
Scanner uses laser-beam to stroke across pattern of bar code. Different patterns of bars reflect the beam in different ways sensed by a light-sensitive detector
Universal Product Code (UPC) is the most widely known bar coding system

## Slide 23: An Example of UPC Bar Code
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
21000
67520
Product category character 0 – grocery products
3 – drugs and health related products, etc.
Manufacturer/supplier identification number
Specific product code number
0
156

## Slide 24: Magnetic-Ink Character Recognition (MICR)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
MICR is used by banking industry for faster processing of large volume of cheques
Bank’s identification code (name, branch, etc.), account number and cheque number are pre-printed (encoded) using characters from a special character set on all cheques
Special ink is used that contains magnetizable particles of iron oxide
MICR reader-sorter reads data on cheques and sorts them for distribution to other banks or for further processing

## Slide 25: MICR Character Set (E13B Font)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
It consists of numerals 0 to 9 and four special characters
MICR is not adopted by other industries because it supports only 14 symbols
157

## Slide 26: Digitizer
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
157
Input device used for converting (digitizing) pictures, maps and drawings into digital form for storage in computers
Commonly used in the area of Computer Aided Design (CAD) by architects and engineers to design cars, buildings medical devices, robots, mechanical parts, etc.
Used in the area of Geographical Information System (GIS) for digitizing maps available in paper form

## Slide 27: A Digitizer
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Digitizing tablet
Stylus in the form of cross-hair cursor
Table top
158

## Slide 28: Electronic-card Reader
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
158
Electronic cards are small plastic cards having encoded data appropriate for the application for which they are used
Electronic-card reader (normally connected to a computer) is used to read data encoded on an electronic card and transfer it to the computer for further processing
Used together as a means of direct data entry into a computer system
Used by banks for use in automatic teller machines (ATMs) and by organizations for controlling access of employees to physically secured areas

## Slide 29: Speech Recognition Devices
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
158
Input device that allows a person to input data to a computer system by speaking to it
Today’s speech recognition systems are limited to accepting few words within a relatively small domain and can be used to enter only limited kinds and quantities of data

## Slide 30: Types of Speech Recognition Systems
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
158
Single word recognition systems can recognize only a single spoken words, such as YES, NO, MOVE, STOP, at a time. Speaker-independent systems are mostly of this type
Continuous speech recognition systems can recognize spoken sentences, such as MOVE TO THE NEXT BLOCK. Such systems are normally speaker- dependent
(Continued from previous slide..)

## Slide 31: Uses of Speech Recognition Systems
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
For inputting data to a computer system by a person in situations where his/her hands are busy, or his/her eyes must be fixed on a measuring instrument or some other object
For data input by dictation of long text or passage for later editing and review
For authentication of a user by a computer system based on voice input
For limited use of computers by individuals with physical disabilities
159

## Slide 32: Vision-Input Systems
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
159
Allow computer to accept input just by seeing an object.
Input data is normally an object’s shape and features in the form of an image
Mainly used today in factories for designing industrial robots that are used for quality-control and assembly processes

## Slide 33: Commonly Used Output Devices
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
160
Monitors
Printers
Plotters
Screen image projector
Voice response systems

## Slide 34: Types of Output
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
160
Soft-copy output
  Not produced on a paper or some material that can be touched and carried for being shown to others
  Temporary in nature and vanish after use
  Examples are output displayed on a terminal screen or spoken out by a voice response system
Hard-copy output
  Produced on a paper or some material that can be touched and carried for being shown to others
  Permanent in nature and can be kept in paper files or can be looked at a later time when the person is not using the computer
  Examples are output produced by printers or plotters on paper

## Slide 35: Monitors
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
160
Monitors are the most popular output devices used for producing soft-copy output
Display the output on a television like screen
Monitor associated with a keyboard is called a video display terminal (VDT). It is the most popular I/O device

## Slide 36: Monitors
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Monitor
Keyboard
A video display terminal consists of a monitor and a keyboard
160

## Slide 37: Types of Monitors
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Cathode-ray-tube (CRT) monitors look like a television and are normally used with non-portable computer systems
Flat-panel monitors are thinner and lighter and are commonly used with portable computer systems like notebook computers. Now they are also used with non- portable desktop computer systems because they occupy less table space.
160

## Slide 38: Printers
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
160
Most
common output devices for producing hard-copy
output
Dot Matrix Printer
Ink Jet Printer
LASER Printer

## Slide 39: Dot-Matrix Printers
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
161
Character printers that form characters and all kinds of images as a pattern of dots
Print many special characters, different sizes of print and graphics such as charts and graphs
Impact printers can be used for generating multiple copies by using carbon paper or its equivalent
Slow, with speeds usually ranging between 30 to 600 characters per second
Cheap in both initial cost and cost of operation

## Slide 40: Formation of Characters as a pattern of dots
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
161

## Slide 41: A Dot Matrix Printer
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
161

## Slide 42: Inkjet Printers
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
161
Character printers that form characters and all kinds of images by spraying small drops of ink on to the paper
Print head contains up to 64 tiny nozzles that can be selectively heated up in a few micro seconds by an integrated circuit register
To print a character, the printer selectively heats the appropriate set of nozzles as the print head moves horizontally
Can print many special characters, different sizes of print, and graphics such as charts and graphs
(Continued on next slide)

## Slide 43: Inkjet Printers
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Non-impact printers. Hence, they cannot produce multiple copies of a document in a single printing
Can be both monochrome and color
Slower than dot-matrix printers with speeds usually ranging between 40 to 300 characters per second
More expensive than a dot-matrix printer
162
(Continued from previous slide..)

## Slide 44: An Inkjet Printers
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
162
Print head of ink jet printer

## Slide 45: Drum Printers
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
162
Line printers that print one line at a time
Have a solid cylindrical drum with characters embossed on its surface in the form of circular bands
Set of hammers mounted in front of the drum in such a manner that an inked ribbon and paper can be placed between the hammers and the drum
Can only print a pre-defined set of characters in a pre- defined style that is embossed on the drum
Impact printers and usually monochrome
Typical speeds are in the range of 300 to 2000 lines per minute

## Slide 46: Printing Mechanism of a Drum Printer
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Solid cylindrical drum with embossed characters
Hammers (one for each band)
Paper
Ribbon
W W W W W W W W W W W W W W V V V V V V V V V V V V V V
U U U U U U U U U U U U U U
T T T T T T S S S S S S R R R R R R
T T T T T T T T S S S S S S S S R R R R R R R R
Q Q Q Q Q Q Q Q Q Q Q Q Q Q
P P P P P P P P P P P P P P O O O O O O O O O O O O O O
N N N N N N N N N N N N N N
Total number of bands is equal to the maximum number of characters (print positions) on a line
163

## Slide 47: Chain/Band Printers
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
163
Line printers that print one line at a time
Consist of a metallic chain/band on which all characters of the character set supported by the printer are embossed
Also have a set of hammers mounted in front of the chain/band in such a manner that an inked ribbon and paper can be placed between the hammers and the chain/band

## Slide 48: Chain/Band Printers
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Can only print pre-defined sets of characters that are embossed on the chain/band used with the printer
Cannot print any shape of characters, different sizes of print, and graphics such as charts and graphs
Are impact printers and can be used for generating multiple copies by using carbon paper or its equivalent
Are usually monochrome
Typical speeds are in the range of 400 to 3000 lines per minute
164

## Slide 49: Laser Printers
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
164
Page printers that print one page at a time
Consist of a laser beam source, a multi-sided mirror, a photoconductive drum and toner (tiny particles of oppositely charged ink)
To print a page, the laser beam is focused on the electro statically charged drum by the spinning multi-sided mirror
Toner sticks to the drum in the places the laser beam has charged the drum’s surface.
Toner is then permanently fused on the paper with heat and pressure to generate the printer output
Laser printers produce very high quality output having resolutions in the range of 600 to 1200 dpi
(Continued on next slide)

## Slide 50: Laser Printers
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Can print many special characters, different sizes of print, and graphics such as charts and graphs
Are non-impact printers
Most laser printers are monochrome, but color laser printers are also available
Low speed laser printers can print 4 to 12 pages per minute. Very high-speed laser printers can print 500 to 1000 pages per minute
More expensive than other printers
165
(Continued from previous slide..)

## Slide 51: A Laser Printers
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
164

## Slide 52: Plotters
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
165
Plotters are an ideal output device for architects, engineers, city planners, and others who need to routinely generate high-precision, hard-copy graphic output of widely varying sizes
Two commonly used types of plotters are:
  Drum plotter, in which the paper on which the design has to be made is placed over a drum that can rotate in both clockwise and anti-clockwise directions
  Flatbed plotter, in which the paper on which the design has to be made is spread and fixed over a rectangular flatbed table

## Slide 53: A Drum Plotter
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Paper
Design drawn on the paper
166

## Slide 54: A Flatbed Plotter
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Design drawn on the paper
Paper
166

## Slide 55: Screen Image Projector
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
166
An output device that can be directly plugged to a computer system for projecting information from a computer on to a large screen
Useful for making presentations to a group of people with direct use of a computer
Full-fledged multimedia presentation with audio, video, image, and animation can be prepared and made using this facility

## Slide 56: Voice Response Systems
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
167
Voice response system enables a computer to talk to a user
Has an audio-response device that produces audio output
Such systems are of two types:
  Voice reproduction systems
  Speech synthesizers
(Continued on next slide)

## Slide 57: Voice Reproduction Systems
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
167
(Continued from previous slide..)
Produce audio output by selecting an appropriate audio output from a set of pre-recorded audio responses
Applications include audio help for guiding how to operate a system, automatic answering machines, video games, etc.

## Slide 58: Speech Synthesizers
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
168
Converts text information into spoken sentences
Used for applications such as:
  Reading out text information to blind persons
  Allowing those persons who cannot speak to communicate effectively
  Translating an entered text into spoken words in a selected language

## Slide 59: Key Words/Phrases
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
168
Bard code reader
Cathode Ray Tube (CRT)
Chain/Band printer
Data scanning device
Digitizer
Digitizing tablet
Dot-Matrix printer
Drum plotter
Drum printer
Electronic card reader
Electronic Pen
Flatbed plotter
Flatbed Scanner
Graphical User Interface
Hand-held scanner
Hard-copy output
Image Scanner
Information Kiosk
Inkjet printer
Input/Output device
Joystick
Keyboard device
Laser printer
Magnetic-Ink Character Recognition (MICR)
Monitor
Mouse
Optical Character Recognition (OCR)
Optical Mark Reader (OMR)
Peripheral device
Phonemes
Plotter
Point-and-draw device
Printer
QWERTY keyboard
Screen Image Projector
(Continued on next slide)

## Slide 60: Key Words/Phrases
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Soft-copy output
Speech synthesizer
Stylus
Touch Screen
Trackball
Universal Product Code (UPC)
Video Display Terminal (VDT)
Vision-input system
Voice recognition device
Voice reproduction system
Voice response system
168
(Continued from previous slide..)