## Slide 1: C is for Configuration

## Slide 2: Introduction
The need of Conf. management.
5 main parts of conf. management.
Local (LAN) and Service Provider variants.
Other considerations.

## Slide 3: Configuration Management
The process in which data is gathered from the network for use in the configuration of network devices.
Tasks:
  Documenting the network layout.
  Documenting the configuration of devices.
  Modifying the network configuration on the fly.

## Slide 4: Configuration
The configs YOU put on to your routers
Not the IOS, Protocols
This information not readily replaceable
You can get hold of an IOS but not on a config.
Needs Management.

## Slide 5: 5 Main Functions
Configured managed resources
Auditing the network
Synchronising management info with Management S/W or
Backing up and restoring configuration
Managing S/W images.

## Slide 6: Configuring Managed Resources
You’ve been doing this
Routers and network devices need to be configured for use according to YOUR policies
2 parts:
  Your Initial Config.
  Future Automated Config.

## Slide 7: Initial Config
Setting up the networking devices to do what it is you want them to do
Making the network “workable” according to organisation policy
Examples – routing protocols, adding networks, configuring layer 2 technologies (Ethernet, TR, ADSL, etc.)
Getting the network working

## Slide 8: User Config
Consider ADSL
– Someone takes the customer order:
  Tel no
  Speed
  Download limit
  Upload limit
  IP addresses, etc
– Lots of settings and lots of customers
– Need an automated system to set this up – a configuration management system

## Slide 9: “User” conf. contd….
Also need internally for an organisation
– Perhaps set up:
• Office PC
• Laptop
• VPN
• Extension no,
• Resources user is allowed to access, etc.

## Slide 10: Why?
Initial config – we need a set of configs that we can revert back to if necessary
User config – to provide services uniformly, securely without large staffing requirement

## Slide 11: Auditing
Are your network devices still there?
Are the networks they are connected to functioning OK?
Did config commands take?
Essential for service provider – unable to visit all sites!

## Slide 12: Auditing contd…
Manual Discovery: Often the only way of determining some features of the network. Especially when looking at intermittent links such as redundant systems and services.
− Difficult, error prone, time consuming, costly and monotonous.
Auto-discovery: Tools to allow you to automatically map the network, detect configuration.

## Slide 13: Auto Discovery Examples
A simple port-scanner to find every IP address in a given range and report a list of the available hosts and services.
Build a complete network map and identify boundaries and firewalls as well as use proprietary protocols such as CDP (Cisco Discovery Protocol).

## Slide 14: OS Fingerprinting
Software: Exploits various ambiguous operations in communications protocols such as TCP, ICMP and UDP.

## Slide 15: Service Identification
Service and Version Discovery: Try a number of standard tricks to determine which software and version are operating on a given socket.
Techniques:
− Null scan (wait for a set time)
− SPAM (send common version $)
− UDP Get Requests

## Slide 16: Boundary Checking
Fire-walking: Techniques designed to analyse responses from routers and firewalls to determine what packets will and won't be forwarded.

## Slide 17: Gathering The Data!!
Basic Tools
− Traceroute : mapping routes between networks
− Ping: check the availability of hosts, networks
− Nmap: port-scanner and fingerprinting tool
More Advanced:
− Net Tools Pro: Mapping, Fingerprinting and Autoconfigure
− SNMP: Read and set managed objects remotely to map the contents of the network
  − RMON: Capture large chunks of traffic and log where protocols are going

## Slide 18: Synchronization
• Need our management s/w to have an up to date network map
• Useless if we have to wait for it to map every device every time we use it!
• From Manageability
• Two views:
– Network is the master (most popular)
– Management system is master (telecomms providers)

## Slide 19: Synchronization contd…
Need to:
– Reconcile
– Re-provision
– Discrepancy reporting

## Slide 20: Backup and Restore
• Must be able to back up and restore your configs – preferably from a remote location
• Critical part of config management
• Version control
• Store off site?

## Slide 21: Management of S/W Images
Routers/net devices use OS’s (cisco is IOS) Variable features, variable support.
Routers have limited proc power, memory, etc
Sometimes shouldn’t have some feature sets on a router – if it doesn’t need them

## Slide 22: Further Reading
Chapter 5 Clemm