|  | IQRA NATIONAL UNIVERSITY, PESHAWAR |
| --- | --- |

D E P A R T M E N T  O F  C I V I L  E N G I N E E R I N G

MID Term Examination (Summer Semester 2020)

Subject:  Engineering Hydrology and Water Management         	                  Duration: 90 Minutes

Instructor: Engr. Fawad Ahmad

Total Marks: 30

Note: Attempt all questions.  Draw sketches where necessary.

Q.NO(01)                                                                                                                (10)

| A | CLO-2 | Calculate evaporation in mm/day using mass transfer approach from an open water surface in a region where air pressure is 115.21 KN/m2. The vapour pressure of water is 5.69 KN/m2 and that of air is 2.54 KN/m2. The wind speed measured at elevation of 3.44 m above water surface is 2.88 m/sec. The density of water and air may be taken as 1000 kg/m3 and 1.34 kg/m3. Von Karman Constant=0.40 Height of Surface roughness = 0.46 mm | 10 |
| --- | --- | --- | --- |

Q.NO(02)                                                                                                                (10)

| A | CLO-1 | Define: Hydrologic Equation Relative Humidity Lapse Rate Meterology Precipitation | 5 |
| --- | --- | --- | --- |
| B | CLO-1 | Write the uses of precipitation data. Also explain the types of precipitation in detail. | 2.5 |
| C | CLO-1 | Explain the mechanism of Floating type rain guage | 2.5 |

Q.NO (03)                                                                 		                                (10)

| A | CLO-2 | Using thiesen polygon Method to find the Average Precipitation Rain Guage Station A B C D E F G Polygon area (Km2) 12 71 42 57 13 34 88 Precipitation (mm) 23.64 31.18 18.52 21.87 22.35 29.18 38.22 | 5 |
| --- | --- | --- | --- |
| B | CLO-2 | Using Isohytel Method Find the Average Precipitation Isohytes (cm) 16.25 22.35 18.61 12.47 16.12 17.12 19.18 20.31 Area Between Isohytes (Km2) 14 35 92 72 44 19 52 | 5 |

********************************Best of Luck**********************************