## Slide 1
TRANSPORTATION PLANNING
Lecture 4

## Slide 2: To Start With
Travel Demand modeling consists of
  Standard models by DOTs in 90s, ‘trip based models’ as these consider ‘trip’ as basic unit of travel.
  Best practice advanced models by progressive planning organizations, eg motorized society modal choice models.
  Alternate paradigm, based upon research, activity base approach, used ‘trip chain concept’, introduction of life style of travel, behavioral, started in 70s and gained momentum.
  Special purpose models, specific issue in limited context.

## Slide 3: Sequence of Activities
Land-Use survey
Travel survey
Trip Generation Equations
Captive Modal Split Model
Trip Distribution Model
Choice Modal Split Model
Route Assignment by Mode
Check against Measured Volumes
Land-Use Allocation
Zonal Trip ends
Trip ends by Mode
O-D Volumes by Mode
Route Assignment by Mode
Volumes by Link and Mode
Alternative Transport Systems

## Slide 4: Background
Trip Generation means” to forecast the number of personal trips that will begin or end in each TAZ for a typical day in target year
Dependent Variable (Base year trips)
Independent Variable (Land use/ socio economic factors)
Calibration (Base year observations and surveys) Relationship between variables and travel quantified, numerical parameters estimated
Calibrated model used for predictive purposes based upon land use and socioeconomic projections in target year
Trip ends Qij / Tij or PI and AJ

## Slide 5: Trip Purpose
Trip purposesHB or NHB
  Home based School
  Home based Work
  Home based Shopping
  Home based Recreational
  Non Home based
Commercial, Light, Medium or Heavy
Separate estimation for each
All have different character
Travel behaviour depends upon trip purpose

## Slide 6: Zonal Based verses Household Based Models
Zonal based (Aggregate)
Zones be accurately delineated.
Smaller zones.
Zonal attributes
  Population Average income
  Average vehicle ownership
  Accuracy affected
Sample survey expanded.
Leads to ‘Zonal total trip ends”
Household based (Disaggregate)
Zones may be larger
Household attributes
  Family income
  Family members
  Vehicles
More accurate
Now even individual based
Sample survey expanded.
Different house groups combined to make ‘Zonal total trip ends”

## Slide 7: PA and OD

## Slide 8: Productions and Attractions
R
NR
R
NR
Zone I
Zone J
O
O
D
D
OD is in terms of direction & PA is in terms of land use
OD easy to collect & PA easy to predict in future

## Slide 9
40
10
21
30
00

## Slide 10
40
10
21
30
00
HBS (Bus)
Home-A
School
Office
Home-B
Recreation
HBW
(Auto)
HBW
(Auto)
HBO
(Auto)
HBO
(Bus)
NHBO
(Auto)
Other information collected may include
Income
Family Size
Car ownership
etc
Network inventory
Knowing sample Population trips determined and checked for survey accuracy
Different matrices may be drawn

## Slide 11
Origin Destination Matrices |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HBS |  |  |  |  |  |  | HBW |  |  |  |  |  |  | HBO |  |  |  |  |  | 
O/D | 10 | 21 | 30 | 40 | Total |  | O/D | 10 | 21 | 30 | 40 | Total |  | O/D | 10 | 21 | 30 | 40 | Total | 
10 |  |  |  | 2 | 2 |  | 10 |  |  |  |  | 0 |  | 10 |  |  |  |  | 0 | 
21 |  |  |  |  | 0 |  | 21 |  |  | 2 |  | 2 |  | 21 |  |  |  |  | 0 | 
30 |  |  |  |  | 0 |  | 30 |  | 2 |  |  | 2 |  | 30 |  |  |  | 4 | 4 | 
40 | 2 |  |  |  | 2 |  | 40 |  | 1 |  |  | 1 |  | 40 |  |  | 3 |  | 3 | 
Total | 2 | 0 | 0 | 2 | 4 |  | Total | 0 | 3 | 2 | 0 | 5 |  | Total | 0 | 0 | 3 | 4 | 7 | 
All HB |  |  |  |  |  |  | NHBO/ NHB |  |  |  |  |  |  | ALL |  |  |  |  |  | 
O/D | 10 | 21 | 30 | 40 | Total |  | O/D | 10 | 21 | 30 | 40 | Total |  | O/D | 10 | 21 | 30 | 40 | Total | 
10 |  |  |  | 2 | 2 |  | 10 |  |  |  |  | 0 |  | 10 |  |  |  | 2 | 2 | 
21 |  |  | 2 |  | 2 |  | 21 |  |  | 1 |  | 1 |  | 21 |  |  | 3 |  | 3 | 
30 |  | 2 |  | 4 | 6 |  | 30 |  |  |  |  | 0 |  | 30 |  | 2 |  | 4 | 6 | 
40 | 2 | 1 | 3 |  | 6 |  | 40 |  |  |  |  | 0 |  | 40 | 2 | 1 | 3 |  | 6 | 
Total | 2 | 3 | 5 | 6 | 16 |  | Total | 0 | 0 | 1 | 0 | 1 |  | Total | 2 | 3 | 6 | 6 | 17 | 
Auto |  |  |  |  |  |  | PT |  |  |  |  |  |  | & So On |  |  |  |  |  | 
O/D | 10 | 21 | 30 | 40 | Total |  | O/D | 10 | 21 | 30 | 40 | Total |  | O/D | 10 | 21 | 30 | 40 | Total | 
10 |  |  |  |  | 0 |  | 10 |  |  |  | 2 | 2 |  | 10 |  |  |  | 2 | 2 | 
21 |  |  | 3 |  | 3 |  | 21 |  |  |  |  | 0 |  | 21 |  |  | 3 |  | 3 | 
30 |  | 2 |  | 4 | 6 |  | 30 |  |  |  |  | 0 |  | 30 |  | 2 |  | 4 | 6 | 
40 |  | 1 |  |  | 1 |  | 40 | 2 |  | 3 |  | 5 |  | 40 | 2 | 1 | 3 |  | 6 | 
Total | 0 | 3 | 3 | 4 | 10 |  | Total | 2 | 0 | 3 | 2 | 7 |  | Total | 2 | 3 | 6 | 6 | 17 | 
Production Attraction Matrices |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HB |  |  |  | NHB |  |  |  | Auto |  |  |  | PT |  |  |  | All Trip Ends |  |  |  | 
Zone | P | A |  | Zone | P | A |  | Zone | P | A |  | Zone | P | A |  | Zone | P | A |  | 
10 |  | 4 |  | 10 |  |  |  | 10 |  |  |  | 10 |  | 4 |  | 10 |  | 4 |  | 
21 |  | 5 |  | 21 | 1 |  |  | 21 | 1 | 5 |  | 21 |  |  |  | 21 | 1 | 5 |  | 
30 | 4 | 7 |  | 30 |  | 1 |  | 30 | 4 | 5 |  | 30 |  | 3 |  | 30 | 4 | 8 |  | 
40 | 12 |  |  | 40 |  |  |  | 40 | 5 |  |  | 40 | 7 |  |  | 40 | 12 |  |  | 
Total | 16 | 16 |  | Total | 1 | 1 |  | Total | 10 | 10 |  | Total | 7 | 7 |  | Total | 17 | 17 |  | 

## Slide 13: Four Step Modeling

## Slide 14: Four Step Modeling
1. Trip Generation modilling
2. Trip Distribution
3. Mode Split
4. Traffic Assignment

## Slide 15: Four Step Modeling
Base Year 2013
Target Year 2028
Person trips interchanges by mode
Vehicle trips by mode
Peak hour flows auto and PT
Trip
generation
Trip
Distribution
Modal Split
Traffic Assignment

## Slide 16
BASE YEAR GENERATIONS
HBS |  |  |  |  | 
O/D | 10 | 21 | 30 | 40 | Total
10 |  |  |  | 2 | 2
21 |  |  |  |  | 0
30 |  |  |  |  | 0
40 | 2 |  |  |  | 2
Total | 2 | 0 | 0 | 2 | 4
HB |  | 
Zone | P | A
10 |  | 4
21 |  | 5
30 | 4 | 7
40 | 12 | 
Total | 16 | 16
BASE YEAR DISTRIBUTION
BASE YEAR MODAL SPLIT
BASE YEAR ROAD NETWORK
BASE YEAR PT ROAD NETWORK
LOS/ BASE YEAR DEFICIENCY
CHANGING TRIPS TO AUTOS/ PT
Four Step Modeling

## Slide 17
PREDICTIONS
BASE YEAR LANDUSE/ SOCIO ECONOMIC FACTORS
BASE YEAR GENERATION (PRODUCTION AND ATTRACTION)
TARGET YEAR LANDUSE/ SOCIO ECONOMIC FACTORS
PREDICTIONS
TARGET YEAR GENERATION (PRODUCTION AND ATTRACTION)

## Slide 18
TARGET YEAR DISTRIBUTION
TARGET YEAR MODAL SPLIT
TARGET YEAR ROAD NETWORK
TARGET YEAR PT ROAD NET WORK
LOS/ TARGET YEAR DEFICIENCY
ASSIGNMENT
CHANGING TRIPS TO AUTOS/ PT
CONSTRUCTION IN TIME
IMPACT STUDIES
Changed attractions, new markets, changed policies, changed priorities

## Slide 19: DEFINITIONS

## Slide 20: 4 STAGES OF TDM

## Slide 21: GREATER TORONTO AREA MODEL

## Slide 22: TRIP DEFINITION

## Slide 23: PRODUCTION-ATTRACTION Example 1

## Slide 24: PRODUCTION-ATTRACTION Example 2

## Slide 25: Trip making and Factors Influencing

## Slide 26: Trip making
A function of three basic factors
  Land use pattern, development in the area.
  Socio economic characteristics of trip making population/ home.
  Nature extent and capabilities of transportation systems.
These independent variables keep changing with time and geographical locations
Once present nature is understood future can be predicted or assessed.

## Slide 27: Factors Influencing
Land use pattern, Development in the Area
  High and low density compared
  Area allocated for shopping, manufacturing, services, hole sale, educational, recreational etc
  Trips can be represented /person,/ acre, / DU
  Small facilities (educational, commercial) may be ignored.
  Large can not be ignored.
  Developments in the area.
  Government policies.

## Slide 28
Socio economic characteristics of trip making population/ home
  Family size
    Relationship exists between family size and trips.
    E.g. 0.8 trips/ day: what about family
  Vehicle ownership
    Satisfy needs
    Social status
    Number
    Accessibility
    System to move on , single vs more, effect on car usage
    Family size large or small, high or low car ownership

## Slide 29
  DU
    Permanent and temporary
    Hotels and hostels
  Occupation
    Employed persons
    Recreational trips for employed and unemployed
    Increase status
  Family Income

## Slide 30
Other Factors
  Property values
  Age group
  Blue and white collars
  Urbanization
  Female working
  Distance from central area
  System quality