## Slide 2
UNIT- 2
Mechanical Modification

## Slide 3
A simple ground improvement technique, where the soil is densified through external compactive effort.
+ water =
Compactive effort

## Slide 4
Advantages of Compaction 1.Increases shear strength 2.Reduces compressibility 3.Reduces permeability 4.Reduces liquefaction potential 5.Controls swelling and shrinking 6.Prolongs durability
Strategies for compaction process are
•In the case of constructed fills, specify placement conditions
(water content, density,depth of layers, etc.)
•Select appropriate equipment (roller compactor, tamping) and method of operation (number of passes, patterns of tamping,etc.).
•Set up adequate control procedures (type and number of tests, statistical evaluation,etc.).

## Slide 5
- to obtain the compaction curve and define the optimum water content and maximum dry density for a specific compactive effort.
Standard
Proctor:
3 layers
25 blows per layer
2.7 kg hammer
300 mm drop
Modified Proctor:
5 layers
25 blows per layer
4.9 kg hammer
450 mm drop
1000 ml compaction mould

## Slide 6: Soil grains densely packed
Water content
Dry density
(d)
optimum water content
d, max
- good strength and stiffness
- low permeability

## Slide 7: What happens to the relative quantities of the three phases
with addition of water?
Dry density (d)
water
soil
difficult to expel all air
lowest void ratio and highest dry density at optimum water content
Water content

## Slide 8: Higher water content or higher compactive effort gives more dispersed fabric.
more dispersed fabric
more dispersed fabric
Water content
Dry density (d)

## Slide 9
Shallow Surface Compaction:
Static rollers:
Smooth steel rollers and pneumatic rollers.
Sheepsfoot rollers.
Grid rollers.
Impact and vibratory equipment:
Tampers,rammers and plate compactors
Vibrating rollers.
Impact rollers.

## Slide 10: Different types of rollers (clockwise from right):
Smooth-wheel roller
Vibratory roller
Pneumatic rubber tired roller
Sheepsfoot roller

## Slide 11
Vibratory and impact compactors for shallow compaction.

## Slide 12: Smooth Wheeled Roller
Compacts effectively only to 200-300 mm; therefore, place the soil in shallow layers (lifts)
19

## Slide 13: Vibrating Plates
for compacting very small areas
  effective for granular soils

## Slide 14: Sheepsfoot Roller
Provides kneading action; “walks out” after compaction
Very effective on clays

## Slide 15: Impact Roller
Provides deeper (2-3m) compaction. e.g., air field
22

## Slide 16
Properties of Compacted Cohesive Soil
OMC increases and MDD decreases with increase in plasticity of soil
Empirical relationships connecting the above to liquid limit, plastic limit are available in literature
Properties of Compacted Cohesionless Soil
MDD is connected to the grain size distribution
parameters

## Slide 17: Strength of Cohesive Soil
CBR as a function of initial water content for a typical
silty clay

## Slide 18
Summary
The methods of shallow
compaction,
properties of compacted soils and its implications in engineering response are discussed.