## Slide 1: Computer Network Management Lecture # 1 by Dr. Sheeraz Ahmed

## Slide 2: Course Contents
• Overview
• Introduction to network programming
• Direct link networks
• Packet switching
• Internetworking
• End-to-end protocols
• Congestion control and resource allocation
• End-to-end data
• Applications

## Slide 3: Network Design
Before looking inside a computer network,
first agree on what a computer network is?
Set of serial lines to attach terminals to mainframe ?
• Telephone network carrying voice traffic ?
• Cable network to disseminate video signals ?
Specialized to handle:
  Keystrokes
  Voice
  Video

## Slide 4: What Distinguishes a Computer Network ?
• Generality
• Built from general purpose
programmable hardware
• Supports wide range of applications

## Slide 5: Applications – Consumers of Networks
• On a simple click, several messages may be exchanged
over the Internet
• In a web browser, 17 messages may be exchanged
  – up to six messages to translate the server name
  – three messages to set up a TCP connection
  – four messages to send HTTP “get” request + response
  – four messages to tear down the TCP connection
• Moreover, millions of messages are exchanged each day by Internet nodes to make their presence and services known

## Slide 6: Applications – the Driving Force
Streaming audio and video is an emerging application
  – Source generates and sends the video stream in messages across the Internet
• Video-on-demand: reads a preexisting movie
  – One-way data transfer
• Videoconferencing: interactive session
  – Very tight timing constraints
• Diversity of applications that can be built on top of the
Internet hint at the complexity of the Internet design
We will study that why networks are designed the way they are?

## Slide 7: Network Overview
• What must a network provide ?
  – connectivity
  – cost-effective sharing
  – functionality
  – performance
• How are networks designed and built ?
  – layering
  – protocols
  – standards

## Slide 8: Perspective
• For network user
  – connectivity: for services required; error free delivery within acceptable time limits
• For network designer
  – efficiency: cost-effective design, fair allocation and efficient use of resources
• For network operator
  – maintenance: easy to administer, fault localization & isolation, usage accounting

## Slide 9: Building Blocks
Nodes: PC, special-purpose hardware…
  – hosts
  – switches
• Links: coax cable, optical fiber…
  – point-to-point
  – multiple access

## Slide 10: Why not connect each node with every other node ?
• Number of computers that can be connected becomes very limited
• Number of wires coming out of each node becomes unmanageable
• Amount of physical hardware/devices required becomes very expensive
• Solution: indirect connectivity using intermediate data forwarding nodes

## Slide 11: Switched Networks
A network can be defined recursively as..

## Slide 12: Switched Networks

## Slide 13: Components of a Network

## Slide 14: Switching Strategies
Circuit switching:
  carry bit streams
  establishes a dedicated circuit
  links reserved for use by communication channel
  send/receive bit stream at constant rate
  example: original telephone network
Packet switching:
  Store and forward messages
  operates on discrete blocks of data
  utilizes resources dynamically according to traffic demand
  send/receive messages at variable rate
  example: Internet

## Slide 15: Addressing and Routing
• Address: byte-string that identifies a node
  – usually unique
• Routing: forwarding decisions
  – process of determining how to forward messages to the destination node based on its address
• Types of addresses
  – unicast: node-specific
  – broadcast: all nodes on a network
  – multicast: some subset of nodes on a network

## Slide 16: Cont…
• A network can be constructed from nesting of networks
• An address is required for each node that is reachable on the network
• Address is used to route messages toward appropriate destination
Hosts know how to reach other hosts on the network
• How should a node use the network for its communication?
• All pairs of hosts should have the ability to exchange messages: cost-effective resource sharing for efficiency

## Slide 17: Multiplexing
Physical links/switches must be shared among users
  – Time-Division Multiplexing (TDM)
  – Frequency-Division Multiplexing (FDM)

## Slide 18: Circuit Switching: FDM and TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 19: Statistical Multiplexing
• On-demand time-division
• Schedule link on a per-packet basis
• Buffer packets in switches that are contending for the link
• Packets from different sources interleaved on link

## Slide 20: Network Taxonomy
Telecommunication
networks
Circuit-switched
networks
FDM
TDM
Packet-switched
networks
Networks
with VCs
Datagram
Networks
Internet provides both connection-oriented (TCP) and
connectionless services (UDP) to apps.

## Slide 21: Internet structure: network of networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., UUNet, BBN/Genuity, Sprint, AT&T), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately
NAP
Tier-1 providers also interconnect at public network access points (NAPs)

## Slide 22: Tier-1 ISP: e.g., Sprint
Sprint US backbone network

## Slide 23: Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other, interconnect at NAP

## Slide 24: Internet structure: network of networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 25: Internet structure: network of networks
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 26: Inter-Process Communication
• Turn host-to-host connectivity into process-to-process communication, making the communication meaningful.
• Fill gap between what applications expect and what the underlying technology provides.

## Slide 27: IPC Abstractions
• Semantics and interface depend on applications
• Request/Reply
  – distributed file systems
    • file servers (FTP)
  – digital libraries / HTTP
    • information retrieval
• Message stream
  – video on-demand
  – video conferencing
    • delay sensitive

## Slide 28: Performance Metrics
• Latency / delay
  – time to send message from point A to point B
  – one-way versus round-trip time (RTT)
• Relative importance, depends on application
  • Large data (file transfer) is bandwidth critical
  • Small data (HTTP) is latency critical

## Slide 29: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 30: Four sources of packet delay
nodal processing
queuing
Transmission delay
Propagation delay
A
B
propagation
transmission
nodal
processing
queueing

## Slide 31: Nodal delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
dprop = propagation delay

## Slide 32: Network Architecture (Layering)
• Use abstractions to hide complexity
• Abstractions naturally lead to layering
• Each layer provides some functionality

## Slide 33: Protocols
• Building blocks of a network architecture
• Each protocol object has two different interfaces
  – service interface: operations on this protocol
  – peer-to-peer interface: messages exchanged with peer
• Term “protocol” is overloaded
  – specification of peer-to-peer interface
  – module that implements this interface
  – peer modules are interoperable if both accurately follow the specifications

## Slide 34: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 35: Message Transmission Using Layers

## Slide 36: Standard Architectures
• Open System Interconnect (OSI) Architecture
  – International Standards Organization (ISO)
  – International Telecommunications Union (ITU)

## Slide 37: OSI Architecture

## Slide 38: Internet Architecture
• TCP/IP Architecture
  – Internet Engineering Task Force (IETF)
    • Culture: implement, then standardize
    • OSI culture: standardize, then implement
  – Became popular with release of Berkeley Software
  Distribution (BSD) Unix; i.e. free software
  – Standard suggestions traditionally debated publicly through “Request For Comments” (RFC’s)

## Slide 39: Internet Architecture
• Layering is not very strict

## Slide 40: Internet protocol stack
application: supporting network applications
  FTP, SMTP, STTP
transport: host-host data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  PPP, Ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 41: Encapsulation
message
segment
datagram
frame
source
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
Hl
M
router
switch

## Slide 42: Network Models

## Slide 43: How Layers Fit Together in Practice

## Slide 44: Protocol Acronyms
• (T)FTP – (Trivial) File Transfer Protocol
• HTTP – Hyper Text Transport Protocol
• SMTP – Simple Mail Transfer Protocol
• TCP – Transmission Control Protocol
• UDP – User Datagram Protocol
• IP – Internet Protocol
• FDDI – Fiber Distributed Data Interface
• ATM – Asynchronous Transfer Mode