## Slide 1: Advance Networking and Management by Prof. Dr. Sheeraz Ahmed

## Slide 2: What Next ?
Start with a simplest possible network
Two nodes connected directly through some suitable medium.

## Slide 3: Direct Link Issues in the OSI and Hardware/Software Contexts
transport
network
data link
physical
session
presentation
application
user-level software
kernel software (device drivers)
reliability
framing, error detection, MAC
encoding
hardware (network adapter)

## Slide 4: Hardware Building Blocks
Nodes
  Hosts: general-purpose computers
  Switches: typically special-purpose hardware
  Routers (connecting networks): varies
Links
  Copper wire with electronic signaling
  Glass fiber with optical signaling
  Wireless with electromagnetic (radio, infrared, microwave) signaling

## Slide 5: Nodes – A Workstation Architecture
CPU
(processor)
Cache $
Memory
I/O bus
Network
adaptor
to network
finite memory (implies limited buffer space)
Device driver managing network adaptor which is using system’s I/O bus
Memory access much slower than CPU speed
memory bus

## Slide 6: Links
Physical media
  twisted pair cable
  coaxial cable
  optical fiber
  space
Media is used to propagate signals
Signals are electromagnetic waves of certain frequency, traveling at speed of light

## Slide 7: Signals Over a Link
Signal is modulated for transmission
  varying freq/amp/ph to receive distinguishable signals
Binary data (0s and 1s) is encoded in a signal
  make it understandable by the receiving host
Bit streams may be transmitted both ways at a time on a point-to-point link
  full-duplex
Sometimes two nodes must alternate link usage
  half duplex

## Slide 8: Which Link to Use ?
Cables
  same room / building / site
insulation
braided conductor
copper core
coax
twisted pair
glass core (fiber)
glass clading
plastic jacket

## Slide 9: Encoding

## Slide 10: Encoding
Signals propagate over a physical medium
  modulate electromagnetic waves
  e.g., vary voltage
Encode binary data onto signals that propagate
Signalling component
Signal
Bits
Node
Node
Adaptor
Adaptor

## Slide 11: Encoding
Problems with signal transmission
  Attenuation: signal power absorbed by medium
  Dispersion: a discrete signal spreads in space
  Noise: random background “signals”
modulator
demodulator
a string of signals
Digital data (a string of symbols)
Digital data (a string of symbols)

## Slide 12: Advantages of Digital Transmission over Analog
Reasonably low-error rates over arbitrary distances
  Calculate/measure effects of transmission problems
  Periodically interpret and regenerate signal
Simpler for multiplexing distinct data types (audio, video, e-mail, etc.)
Examples of modulators-demodulators (modems)
  Electronic Industries Association (EIA) standard RS-232(-C)
  International Telecommunications Union (ITU) standard V.32 96 kbps modem

## Slide 13: Binary Voltage Encoding
NRZ (non-return to zero)
NRZI (NRZ inverted)
Manchester (used by IEEE 802.3, 10 Mbps Ethernet)
4B/5B (8B/10B) in Fast Ethernet

## Slide 14: Non-Return to Zero (NRZ)
Encode binary data onto signals
  e.g., 0 as low signal and 1 as high signal
  voltage does not return to zero between bits
    known as Non-Return to Zero (NRZ)
Bits
NRZ
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0

## Slide 15: Problem: Consecutive 1s or 0s
(Continuous)Low signal (0) may be interpreted as no signal
(Continuous)High signal (1) leads to baseline wander
Unable to recover clock
  sender’s and receiver’s clock have to be precisely synchronized
  receiver resynchronizes on each signal transition
  clock drift in long periods without transition
sender’s clock
receiver’s clock

## Slide 16: Alternative Encodings
Non-Return to Zero Inverted (NRZI)
  make a transition from current signal (switch voltage level) to encode/transmit a “one”
  stay at current signal (maintain voltage level) to encode/ transmit a “zero”
  solves the problem of consecutive ones (shifts to 0s)

## Slide 17: Alternative Encodings
Manchester (in IEEE 802.3 – 10 Mbps Ethernet)
  split cycle into two parts
    send high--low for “1”, low--high for “0”
    transmit XOR of NRZ encoded data and the clock
  only 50% efficient (1/2 bit per transition)

## Slide 18: Different Encoding Schemes
Bits
NRZ
Clock
Manchester
NRZI
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0

## Slide 19: 4B/5B Encoding
Every 4 consecutive bits of data encoded in a 5-bit code (symbol)
  4-bit pattern is “translated” to a 5-bit pattern (not addition)
5-bit codes selected to have no more than one leading 0 and no more than two trailing 0s
  00xxx (8 symbols) and xx000 (4 symbols) are illegal
  5 free symbols (non-data)
Thus, never gets more than three consecutive 0s
Resulting 5-bit codes are transmitted using NRZI
Achieves 80% efficiency

## Slide 20: Modulation
Types of modulation
  Amplitude (AM)
  Frequency (FM)
  Phase / phase shift
  Combination of these (e.g. QAM)

## Slide 21: Amplitude Modulation
idle idle 1 idle idle 0 idle idle
time

## Slide 22: Frequency Modulation
idle idle 1 idle idle 0 idle
time

## Slide 23: Phase Modulation
idle idle 1 idle idle 0 idle idle
time

## Slide 24: Phase Modulation Algorithm
Send carrier frequency for one period
Perform phase shift
Shift value encodes symbol
  value in range [0, 360º]
  multiple values for multiple symbols
  represent as circle
1350 450
2250 3150
1800 00
900
2700
8-symbol example

## Slide 25: Quadrature Amplitude Modulation
Same algorithm as phase modulation
Can also change signal amplitude
2-dimensional representation
  angle is phase shift
  radial distance is new amplitude
Each symbol contains log2 16 = 4 bits
  data rate is thus 4 x 2400 = 9600 bps
450
150
16-symbol example (V.32)

## Slide 26: Bit Rate and Baud Rate
Bit rate is bits per second
Baud rate is “symbols” per second
If each symbol contains 4 bits then data rate is 4 times the baud rate

## Slide 27: What Limits Baud Rate ?
Baud rates are typically limited by electrical signaling properties
No matter how small the voltage or how short the wire, changing voltages takes time
Electronics are slow as compared to optics

## Slide 28: Framing

## Slide 29: Framing
Breaks continuous stream/sequence of bits into a frame and demarcates units of transfer
Typically implemented by network adaptor
  Adaptor fetches/deposits frames out of/into host memory
Frames
Bits
Adaptor
Adaptor
Node B
Node A

## Slide 30: Advantages of Framing
Synchronization recovery
  consider continuous stream of unframed bytes
  recall RS-232 start and stop bits
Multiplexing of link
  multiple hosts on shared medium
  simplifies multiplexing of logical channels
Efficient error detection
  frame serves as unit of detection (valid or invalid)
  error detection overhead scales as log N

## Slide 31: Approaches
Organized by end of frame detection method
Approaches to framing
  sentinel (marker, like C strings)
  length-based (like Pascal strings)
  clock-based
Other aspects of a particular approach
  bit- or byte-oriented
  fixed- or variable-length
  data-dependent or data-independent length

## Slide 32: Framing with Sentinels
*Basic idea: identify end of frame with:
(1) “Frame marker” or(2) special byte or bit pattern
(2)End of frame: special byte or bit pattern
(1)Choice of end of frame marker
  valid data byte or bit sequence e.g. 01111110
  physical signal not used by valid data symbol
8
16
16
8
Beginning sequence
Header
Body
CRC
Ending sequence

## Slide 33: Sentinel Based Approach
Problem: what if special pattern appears in the payload(*data stream)
Solution: bit stuffing
  sender: insert 0 after five consecutive 1s
  receiver: delete 0 that follows five consecutive 1s
Node B
Node A
x
0
1
1
1
1
1
x
1
1
1
1
1
0
0
x
0
1
1
1
1
1
0
x
1
1
1
1
1
0

## Slide 34: Sentinel Based Approach
Sentinel based framing examples
  High-Level Data Link Control (HDLC) protocol
  Point-to-Point Protocol (PPP)
  ARPANET IMP-IMP protocol
  IEEE 802.4 (token bus)

## Slide 35: Length-based Framing
Include payload length in header
e.g. RS-232 (bit-oriented, implicit fixed length)
Problem: count field corrupted
Solution: catch when CRC fails
8
14
8
SYN
SYN
Class
Length
8
42
Header
16
Body
CRC

## Slide 36: Error Detection

## Slide 37: Error Detection
Why we need it ?
  To avoid retransmission of whole packet or message
What to do if error detected ?
  Discard, and request a new copy of the frame:
    explicitly or implicitly
  Try to correct error, if possible

## Slide 38: Error Detection
Validates correctness of each frame
Errors checked at many levels
Demodulation of signals into symbols (analog)
Bit error detection/correction (digital)—our main focus
  Within network adapter (CRC check)
  Within IP layer (IP checksum)
  Possibly within application as well

## Slide 39: Error Detection: How ?
How to detect error ?
  Add redundant information to a frame to determine errors
Transmit two complete copies of data
  n redundant bits for n-bit message
  Error at the same position in two copies go undetected

## Slide 40: Error Detection: How ?
We want only k redundant bits for an n-bit message, where k < < n
  In Ethernet, 32-bit CRC for 12,000 bits (1500 bytes)
k bits are derived from the original message
Both the sender and receiver know the algorithm

## Slide 41: Digital Error Detection Techniques
Two-dimensional parity
  Detects up to 3-bit errors
  Good for burst errors
Internet checksum (used as backup to CRC)
  Simple addition
  Simple in software
Cyclic redundancy check (CRC)
  Powerful mathematics
  Tricky in software, simple in hardware
  Used in network adapter

## Slide 42: Two-Dimensional Parity
Adding one extra bit to a 7-bit code to balance 1s
extra parity byte for the entire frame
Catches all 1-, 2- and 3-bit errors and most 4-bit errors
14 redundant bits for a 42-bit message, in the example
1011110
1
1101001
0
0101001
1
1011111
0
0110100
1
0001110
1
1111011
0
Parity
bits
Parity
byte
Data

## Slide 43: Two-Dimensional Parity
0
1
0
0
0
1
1
1
0
1
1
0
0
0
1
1
0
1
1
0
1
1
1
1
0
1
1
0
0
0
0
0
1
0
0
1
0
0
1
1
0
1
1
0
1
1
0
0
1
1
0
1
0
1
0
0
0
1
1
0
1
1

## Slide 44: Internet Checksum Algorithm
Not used at the link level but provides same sort of functionality as CRC and parity
Idea:
  Add up all words (16-bit integers) that are transmitted
  Transmit the result (checksum) of that sum
  Receiver performs the same calculation on received data and compares the result with the received checksum
  If the results do not match, an error is detected
16 redundant bits for a message of any length
Weak protection, accepted as a last line of defense

## Slide 45: Cyclic Redundancy Check
Theory
based on finite-field (binary-valued) arithmetic
bit string represented as polynomial
coefficients are binary-valued
divide bit string polynomial by generator polynomial to generate CRC
Practice
bitwise XOR’s

## Slide 46: Cyclic Redundancy Check
Add k bits of redundant data to an n-bit message
  want k << n
  e.g., k = 32 and n = 12,000 (1500 bytes)
Represent n-bit message as n-1 degree polynomial
  e.g., MSG=10011010 as M(x) = x7 + x4 + x3 + x1
  Sender and receiver exchange polynomials
Let k be the degree of some agreed-upon divisor/ generator polynomial
  e.g., C(x) = x3 + x2 + 1

## Slide 47: Cyclic Redundancy Check
Transmit polynomial P(x) that is evenly divisible by C(x)
  shift left k bits, i.e., M(x)xk
  add remainder of M(x)xk / C(x) into M(x)xk
Receiver receives polynomial P(x) + E(x)
  E(x) = 0 implies no errors
Receiver divides (P(x) + E(x)) by C(x); remainder will be zero ONLY if:
  E(x) was zero (no error), or
  E(x) is exactly divisible by C(x)

## Slide 48: CRC Example - Sender
C(x) = x3+x2+1 = 1101  generator
M(x) = x8 + x6 + x5 + x4+1 = 101110001  message
1101 ) 101110001000
1101
1101
1101
00001000
1101
101 remainder

## Slide 49: CRC Example - Receiver
C(x) = x3+x2+1 = 1101  generator
M(x) = x11+x9+x8+x7+x3+x2+1 = 101110001101  message
1101 ) 101110001101
1101
1101
1101
00001101
1101
0 correct !

## Slide 50: CRC Example - Receiver
C(x) = x3+x2+1 = 1101  generator
M(x) = x11+x9+x8+x7+x3+x2+1 = 101110001101  message
1101 ) 101101001101
1101
1100
1101
1100
1101
1110
1101
111 incorrect !
Two bits are flipped

## Slide 51: CRC Example - Receiver
C(x) = x3+x2+1 = 1101  generator
M(x) = x11+x9+x8+x7+x3+x2+1 = 101110001101  message
1101 ) 101101011101
1101
1100
1101
1101
1101
1101
1101
0 incorrectly correct !!!
Three bits are flipped

## Slide 52: Error Detection or Correction ?
Detection implies discarding message and waiting for retransmission
  uses bandwidth
  introduces latency
Error correction requires more redundant bits to send all the time : error-correcting code (FEC)
Error correction is useful when:
  errors are quite probable (wireless links)
  retransmission cost is too high (latency in satellite link, multicast)

## Slide 53: End of Lecture 3