## Slide 1: WIRELESS COMMUNICATION
CELLULAR CONCEPTS
Engr. Latif Jan
IQRA NATIONAL UNIVERSITY

## Slide 2: WHAT IS WIRELESS COMMUNICATION?
Transmitting/receiving voice and data using electromagnetic waves in open space.
The information from sender to receiver is carried over a well defined frequency band(channel).
Each channel has a fixed frequency bandwidth & capacity(bit rate).
Different channels can be used to transmit information in parallel and independently.

## Slide 3: How communication takes place?
Transmitting signal
Received signal
satellite
Transmitting antenna
Receiving
antenna

## Slide 4: TYPICAL FREQUENCIES
FM RADIO 88 MHZ
TV BROADCAST 200 MHZ
GSM PHONES 900 MHZ
GPS 1.2 GHZ
PCS PHONES 1.8 GHZ
BLUETOOTH 2.4 GHZ
Wi-Fi 2.4 GHZ

## Slide 5: WHY WIRELESS COMMUNICATION?
Freedom from wires.
No bunch of wires running from here and there.
“Auto Magical” instantaneous communication without physical connection setup e.g.- Bluetooth, Wi-Fi.
Global coverage
Communication can reach where wiring is infeasible or costly
e.g.- rural areas,buildings,battlefield,outerspace.
Stay connected,flexiblity to connect multiple devices.

## Slide 6: TYPES OF WIRELESS COMMUNICATION?
RADIO TRANSMISSION:- easily generated, Omni-directional , travel long distance , easily penetrates buildings.
PROBLEMS:- frequency dependent , relatively low bandwidth for data communication , tightly licensed by government.
MICROWAVE TRANSMISSION:- widely used for long distance communication , give high S/N ratio , relatively inexpensive.
PROBLEMS:- don’t pass through buildings , weather and frequency dependent.

## Slide 7: TYPES CONTINUED….
INFRARED AND MILIMETER WAVES:-
widely used for short range communication , unable to pass through solid objects , used for indoor wireless LANs , not for outdoors.
LIGHT WAVE TRANSMISSION:- unguided optical signal such as laser , unidirectional , easy to install , no license required.
PROBLEMS:- unable to penetrate rain or thick fog , laser beam can be easily diverted by air.

## Slide 8: CURRENT WIRELESS SYSTEMS
CELLULAR SYSTEM
WIRELESS LANs
SATELLITE SYSTEM
PAGING SYSTEM
PANs(BLUETOOTH)

## Slide 9: What is cellular system?
Definition
Wireless communication technology in which several small exchanges (called cells) equipped with low-power radio antennas (strategically located over a wide geographical area) are interconnected through a central exchange. As a receiver (cell phone) moves from one place to the next, its identity, location, and radio frequency is handed-over by one cell to another without interrupting a call.
Practical

## Slide 10: Cellular system basic concept?
High capacity is achieved by limiting the coverage of each base station to a small geographic region called a cell.
Same frequencies timeslots/codes are reused by spatially separated base stations.
A switching technique called handoff enables a call to proceed uninterrupted when one user moves from one cell to another.
Neighboring base stations are assigned different group of channels so as to minimize the interference.

## Slide 11: Cellular system basic concept contd…
By systematically spacing base stations and the channel groups may be reuse as many number of times as necessary.
MSC
CELLS
PSTN
SUBSCRIBER UNIT
BASE STATIONS
Coverage area

## Slide 12: Hand over ?
BSC
BS1
BS2
BS3
Connect to Bs1 & start calling
Out of BS1 coverage & connect to BS2
Out of BS2 coverage & connect to BS3
Call ended

## Slide 13: FREQUENCY REUSE THE NEED?
Cellular radio systems rely on intelligent allocation and reuse of channels throughout the coverage area.
Each base station is allocated a group of radio channels to be used within the same geographical area of its cell.
Neighboring base stations are given different channel allocation from each other.
The design procedure of allocating channel groups for all of the cellular BS within a system is called frequency reuse or frequency planning.

## Slide 14: Example of frequency reuse?
Co channel cells
Co channel cells

## Slide 15: How to find co -channel cell?
Co channels
60 degree
u
v
D

## Slide 16: The geometry of hexagon?
Axes u and v intersect at 60 degree.
Unit scale is the distance between center cells.
If cell radius to point of hexagon is R then 2Rcos30=1
Or R = 1/√3. to find the distance of a point P(u , v) from the origin we use x-y to u-v coordinate transformation.
R² = x² + y²
x=ucos30˚
y=u+vsin30˚

## Slide 17: Geometry contd…
Using this equation to locate co-channel cells we start from reference cell and moves i hexagon along u axis then j hexagon along the v axis.
Hence the distance between co-channel cells in adjacent cluster is given by D = √(i²+ij+j²)
The number of cells in a cluster N is given by
N = √(i²+ij+j²) where i and j are integers.
Hence the possible values of N are 1 , 3 , 4 , 7 , 12……

## Slide 18: Co-channel location
Formation of cluster for N=7
Suppose i=2 and j=1 will give co channel cell
Same color showing co-channel cells.
i=2
j-=1
Co channel cells

## Slide 19
END of Slides….