## Slide 1: Performance management in Network management system
Lecture-2

## Slide 2: Performance Management system
Performance Management provides functions to evaluate and report upon the behavior of telecommunication equipment and the effectiveness of the network or network element. Its role is to gather and analyze statistical data for the purpose of monitoring and correcting the behavior and effectiveness of the network, network elements, or other equipment and to aid in planning, provisioning, maintenance and the measurement of quality.

## Slide 3: Performance Management
Performance management tries to quantify performance by using some measurable quantity such as :
Capacity
Traffic
Throughput
Response time

## Slide 4: Capacity
Every network has limited capacity The performance management system ensure that the network is not used above its capacity If the network is used above its capacity, the data rate will decrease and blocking may occur.

## Slide 5: Traffic
Traffic ca be measured in two ways:
Internally : measured by the number of packets travelling inside the
network Externally : measured by exchange of packets outside the network

## Slide 6: Throughput
Performance management monitors the throughput to make sure that it is not reduced to unacceptable levels.

## Slide 7: Response time
Response time is normally measured from the time a user requests a service to the time the service is granted It can be affected by capacity and traffic

## Slide 8: Performance management functions tasks
Performance management includes functions to:
logs of system state histories=> maintain and examine
system performance under natural and artificial conditions=> determine
system modes of operation for conducting performance management activities =>alter
statistical information => gather

## Slide 9: SNMP
SNMP can be assigned to both performance and accounting and could lead to long theoretical discussions concerning which area they belong to.

## Slide 10: RMON
RMON provides general network utilization details, such as traffic patterns, top talkers, and applications in the network. RMON information can be collected both at the core and at the edge

## Slide 11: ART
ART measures delays between request/response sequences in application flows, such as HTTP and FTP, but it can monitor only applications that use well-known TCP ports. To provide end-to-end measurement, an ART probe is needed at both the client and the server end

## Slide 12: Counters
Counters provide information about data that an application sends and receives over the network

## Slide 13: VoIP
Troubleshooting Cisco VoIP call quality is relatively straight forward with the right monitoring and diagnostic tools to help you identify the cause. The most likely causes include: Jitter resulting from congestion in the LAN or the access link, load sharing, routing table updates, and route flapping Latency as a result of propagation delay, handling delay, queuing delay, router outages or link congestion Packet loss occurring from link failures, traffic congestion leading to buffer overflow in routers, faulty networking hardware and occasionally a misrouted packet.

## Slide 14: SAA
Systems Application Architecture (SAA) was IBM's strategy for enterprise computing in the late 1980s and early 1990s.enterprise SAA defined three layers of service:
Common User Access
Common Programming Interface
Common Communications Support

## Slide 15: Purposes
Purposes of Performance Various performance scenarios:
Baselining
Service Monitoring
Network Performance Monitoring
Device Performance Monitoring

## Slide 16: Baselining
Baselining is the process of studying the network, collecting relevant information, storing it, and making the results available for later analysis
A general baseline includes all areas of the network, such as a connectivity diagram, inventory details, device configurations, software versions, device utilization, link bandwidth, and so on
The baselining task should be done on a regular basis, because it can be of great assistance in troubleshooting situations as well as providing supporting analysis for network planning and enhancements
It is also used as the starting point for threshold definitions, which can help identify current network problems and predict future bottlenecks

## Slide 17: Baselining tasks
Gather device inventory information
Gather statistics (device-, network-, and service-related) at regular intervals
Document the physical and logical network, and create network maps
Identify the protocols on your network
Identify the applications on your network
Monitor statistics over time, and study traffic flows
Collect network device-specific details
Gather server- and (optionally) client-related details
Gather service-related information

## Slide 18: Monitoring concepts
You can distinguish between two major monitoring concepts:
Passive monitoring— Also referred to as "collecting observed traffic," this form of monitoring does not affect the user traffic, because it listens to only the packets that pass the meter. Examples of passive monitoring functions are SNMP, RMON, Application Response Time (ART) MIB, packet-capturing devices (sniffer), and Cisco NetFlow Services.
Active monitoring— Introduces the concept of generating synthetic traffic, which is performed by a meter that consists of two instances. The first part creates monitoring traffic, and the second part collects these packets on arrival and measures them.

## Slide 19: Device Performance
Monitoring Network Element Performance Monitoring From a device perspective, we are mainly interested in device "health" data, such as overall throughput, per-(sub)interface utilization, response time, CPU load, memory consumption, errors, and so forth System and Server Performance Monitoring Low-level service monitoring components:
System: hardware and operating system (OS)
- Network card(s)
- CPU: overall and per system process
- Hard drive disks, disk clusters
- Fan(s)
- Power supply

## Slide 20: Device Performance
- Temperature
- OS processes: check if running; restart if necessary
- System uptime High-level service monitoring components:
- Application processes: check if running; restart if necessary
- Server response time per application
- Optional: Quality of service per application: monitor resources (memory, CPU, network bandwidth) per CoS (class of service) definition
- Uptime per application

## Slide 21: Network Performance Monitoring
Network connectivity and response time can be monitored with basic tools such as ping and traceroute or with more advanced tools such as Ping-MIB, Cisco IP SLA, external probes, or a monitoring application running at the PC or serve

## Slide 22: Network Performance Monitoring
Transmission efficiency
Jitter (delay variation) Network delay Network throughput/capacity Packet loss Utilization (device, network) Network response time

## Slide 23: Network Performance Monitoring
Transmission efficiency
Calculation of transmission efficiency is related to the number of invalid packets; it measures the error-free traffic on the network and compares the rate of erroneous packets to accurate packets

## Slide 24: Network Performance Monitoring
Jitter
jitter is the variation in latency as measured in the variability over time of the packet latency across a network. A network with constant latency has no variation (or jitter).
The standards-based term is "packet delay variation" (PDV). PDV is an important quality of service factor in assessment of network performance.
packet delay variation quality of service

## Slide 25: Network Performance Monitoring
Network delay
Latency = propagation time + transmission time+ queuing time + processing time
Where is
Propagation time = distance/propagation speed and
Transmission time=packet size/ BW

## Slide 26: Network Performance Monitoring
Packet loss
it occurs when one or more packets of data travelling across a computer network fail to reach their destination packets computer network

## Slide 27: Network Performance Monitoring
Utilization (device, network)
Utilization=(total data in bits/bandwidth) *100
Example:
In a channel with BW = 1 Gbps Compare the utilization between a stop-and-wait protocol and go-back-in protocol(with window size =7 ) with a 3KByte packet.

## Slide 28: Service monitoring
Service availability measurements require explicit measurement devices or applications, because a clear distinction between server and service is necessary Service Monitoring

## Slide 29: Service monitoring
From a service perspective, here are significant parameters to monitor:
Key Quality Indicators (KQI)
Jitter (delay variation)
Mean Opinion Score (MOS)
in the case of voice Key Performance Indicators (KPI)
Packet loss
Service delay
Service availability

## Slide 30: Service Monitoring Key Quality Indicators (KQI)
Maintaining a dynamic Data Quality environment involves creating a monitoring and feedback mechanism for quality analysts, data stewards and corporate compliance officers.
Logan Britton provides actionable Data Quality metrics known as Key Quality Indicators or (KQI’s). These are high level indicators in the form of reports and dashboards used to monitor your critical data enabling the implementation of preventative measures

## Slide 31: Service Monitoring
Mean Opinion Score (MOS) in the case of voice
A mean opinion scale (MOS) has been the recommended measure of synthesized speech quality /

## Slide 32: Service Monitoring
Key Performance Indicators (KPI)
is a measurable value that demonstrates how effectively a company is achieving key business objectives Organizations use KPIs to evaluate their success at reaching targets.

## Slide 33: Service Monitoring
Service availability
MTBF, MTTD, MTTR and MTTF are the four parameters required to calculate the availability of a service or an individual component in a specific architecture.
MTBF is the Mean Time Between Faults
MTTD is the Mean Time To Detection
MTTR is the Mean Time To Repair
MTTF is the Mean Time To Failure
Well, once we got this, there are just a few little formula to know :
MTBF = MTTD + MTTR + MTTF
Availability = MTBF / (MTBF + MTTR)

## Slide 34: SLA
A service-level agreement (SLA) is a part of a service contract where a service is formally defined. Particular aspects of the service - scope, quality, responsibilities - are agreed between the service provider and the service user service contract