## Slide 1: Mobile Computing
WEARABLE COMPUTING Part 1

## Slide 2: The Past – The Present

## Slide 3: Steve Mann
1970s, pre-laptop, early computer era.
Building computers he could wear.
Inventor of wearable computing.

## Slide 4: Steve Mann
1991: Started the ”Wearable Computing Project” at MIT.
1995: World’s first covert wearable computer – camera and display concealed in ordinary eyeglasses.
1997: PhD from MIT in the field he himself had invented.
Today: Works at University of Toronto.

## Slide 5: Steve Mann

## Slide 6: What is Wearable Computing?
Mann
  “A wearable computer is a computer that is subsumed into the personal space of the user, controlled by the user, and has both operational and interactional constancy, i.e. is always on and always accessible. Most notably, it is a device that is always with the user, and into which the user can always enter commands and execute a set of such entered commands, and in which the user can do so while walking around or doing other activities”

## Slide 7: What is Wearable Computing?
Seven attributes of wearable computing [Steve Mann, 1998]:
Unmonopolizing of the user’s attention. User can attend to other events.
Unrestrictive to the user. Allows interaction while user carries out normal functions.
Observable by the user. As the system is being worn, there is no reason why the wearer cannot be aware of it continuously… but this contrasts with 1!
  Better phrasing: User can identify computational and non-computational components of their clothing.
Controllable by the user. User can take control at any time.
Attentive to the environment. Can enhance the user’s environment and situational awareness.
Communicative to others. Can be used as a communications medium.
Shares the same physical and situational context as the user.

## Slide 8: Purpose: Mediate Interactions
Wearable computers will help provide a consistent interface to computationally augmented objects in the physical world.
  Example: Gesture Pendant
  One gesture could provide an intuitive command for many devices

## Slide 9: Purpose: Aid Communication
The wearable can also assist in human-to-human communication.
Wearable computers can also help manage interruption in the user’s daily life.

## Slide 10: Purpose: Provide Context-Sensitive Reminders
Instead of simply acting as a virtual secretary, the wearable could be proactive and intimate, listening to the wearer’s conversations and providing reminders as appropriate

## Slide 11: Purpose: Augmented Reality
Augmented reality overlays information-rich virtual realities onto the physical world.
In a sense, augmented reality is a combination of the application domains described previously.
https://www.youtube.com/watch?v=vDNzTasuYEw

## Slide 12: Components of a Wearable Device

## Slide 13: Head-Mounted Display (HMD)
Small screen, typically covering one of your eyes.
Works like an ordinary monitor, providing an image floating in the air in front of you.
Transparent vs opaque.

## Slide 14: Camera (& Sensors)
Suitable placement
  Head, follows user’s gaze.
  Shoulder, more stable.

## Slide 15: Input Device
Keyboard
  Canesta’s IR keyboard.
  Arm-strapped keyboard.
  FrogPad
  Twiddler chording keyboard
Mouse
  Twiddler, again.
BrainGate

## Slide 16: Input Device
Gestures
  Gesture Pendant (controlling smart homes)
Voice recognition
  Siri
Multi-modal interfaces
Something new?

## Slide 17: Output device
Sight – Visual output
  HMD, wristwatch...
Hearing – Audio/sound/speech/music
  Speakers, earplug/headset...
Touch – Tactile feedback
Taste and smell

## Slide 18: The Computer Itself
Anything small, but powerful enough
  Smartphones
  Smartwatches
  Embedded computers

## Slide 19: Network Connection
Benefits of having a network
  Access to the Internet
  Communication
  Localization
Wireless network connection
  WLAN
  3G, 4G, LTE
  Bluetooth, ZigBee
  InfraRed

## Slide 20: Other Challenges
Connecting all pieces
  Wires (embedded into clothing?), wireless (security?), body as conduit
Power supply
  Batteries (rechargeable; solar power)
  Human powered devices
    Body heat, 0.6 – 4.8W (wetsuit clothes)
    Breath, 0.4 – 2.5W (pressure mask)
    Blood pressure, 0.2W
    Limb motion, 0.3 – 1.5W
    Finger motion, 0.019W (keyboard typing)
    Walking, 5 – 8W (shoe generator)
Heat dissipation

## Slide 21: Examples
Technicians
  Blueprints, etc.
Field workers
  Access to information given by remote experts.
Military personnel
  Soldiers, monitoring health, equipment, etc.
  Maps and terrain.
  Infrastructure (sewers, roads) in urban areas.
Researchers

## Slide 22: Examples
Wearables for sports training
Karate trainees are instrumented with acceleration sensors.
Sensor data is translated directly into sound output.
Trainees can now ‘hear’, as well as see instructor’s movements.
Trainees can also hear themselves: attempt to match own sound to sound of instructor.
Martial arts training is about reproducing patterns over time, not just matching static poses; therefore, sound is a useful sensory stimuli to introduce to training.
Result: Trainees with system tended to learn faster than trainees without system.

## Slide 23: Examples
Wearables for the military: Future Force Warrior (FFW)
Onboard physiological/medical sensor suite to accelerate casualty care
Netted communications to maximize robustness and integration of small teams
Embedded training (similar to martial arts example?)
Enhanced situational awareness (heads-up display?)
Synchronized firing of weapons from team.
Bone conduction technology: “talking and speaking without sound or hearing”

## Slide 24: Examples: Smartphone Extensions & Fitness Trackers