## Slide 1: ADVANCE ENGINEERING SURVEYING LECTURE 5
By
Engr. Abdul Farhan
Lecturer Department of Civil Engineering
Iqra National University, Peshawar

## Slide 2: TOPICS TO BE COVERED
  Compound Curve
  Problems related to Compound Curve

## Slide 3: Curves Compound Curves
A compound curve consist of 2 arcs of different radii bending in the same direction and lying on the same side of their common tangent. Then the center being on the same side of the curve.
RS = Smaller radius RL = Larger radius
TS = smaller tangent length = BT1 TL = larger tangent length = BT2
𝛼 = deflection angle b/w common tangent and rear tangent
𝛽 = angle of deflection b/w common
tangent and forward tangent
N = point of compound curvature KM = common tangent

## Slide 4: Curves
Compound Curves
Elements of Compound Curve
∅ = 𝛼 + 𝛽
1 S
2
KT = KN =R tan(𝛼)
2 L
2
MN = MT = R tan (𝛽)
From ∆BKN, by sine rule
=
𝐵𝐾 𝑀k𝐾
sin 𝛽 sin 𝐼
=
𝐵𝐾 𝑀𝐾
sin 𝛽 sin(180o – (𝛼 +𝛽))
BK = 𝑀𝐾 sin 𝛽 sin(180o – (𝛼 +𝛽))
BM = 𝑀𝐾 sin 𝜶 sin(180o – (𝛼 +𝛽))
180o - (𝛼 +𝛽) = I
180o – ∅ = I

## Slide 5: Curves
Compound Curves
Elements of Compound Curve
TS = BT1 = BK + KT1
TS = BT1 =
𝑀𝐾
sin 𝛽
sin(180o – (𝛼 +𝛽))
S
2
+ R tan (𝛼)
TL = BT2 =
𝑀𝐾 sin 𝜶
sin(180o – (𝛼 +𝛽))
L
2
+ R tan (𝛽)
Of the seven quantities RS, RL, TS, TL, ∅, 𝛼, 𝛽
four must be known.

## Slide 6: Curves
1 L
𝛼
2
o
KT = KN = R tan ( ) = 600 tan(40 /2)
KT1 = KN = 218.38 m
2 S
𝛽
2
o
MN = MT = R tan( ) = 400 tan(35 /2)
MN = MT2 = 126.12 m
KM = MT2 + MN = 218.38 + 126.12 KM = 344.50 m
Compound Curves
Problem: Two tangents AB & BC are intersected by a line KM. the angles AKM and KMC are 140o & 145o respectively. The radius of 1st arc is 600m and of 2nd arc is 400m. Find the chainage of tangent points and the point of compound curvature given that the chainage of intersection point is 3415 m.
Solution:
𝛼 = 180o – 140o = 40o
𝛽 = 180o – 145o = 35o
∅= 𝛼 + 𝛽 = 75o
I = 180o – 75o = 105o
71

## Slide 7: Curves
Solution:
Fin ∆BKM, by sin rule
=
𝐵𝐾 𝑀𝐾
sin 𝛽 sin(𝐼)
sin(I)
sin 105𝑜
BK = 𝑀𝐾 sin 𝛽 = 344.50 𝑥 𝑠𝑖𝑛35𝑜 = 204.57 m
sin(𝐼I)
sin 105𝑜
BM = 𝑀𝐾 sin 𝛼 = 344.50 𝑥 𝑠𝑖𝑛40𝑜 = 229.25 m
L
180𝑜 180𝑜
TL = KT1 + BK = 218.38 + 204.57 = 422.95 m TS = MT2 + BM = 126.12 + 229.25 = 355.37 m
L = 𝜋 𝑅𝐿 𝛼 = 𝜋 𝑥 600 𝑥4 0 = 418.88 m
S
L =
𝑆
180𝑜
𝜋 𝑅 𝛽 𝜋 𝑥 400 𝑥 30
180𝑜
= = 244.35 m
Compound Curves

## Slide 8: Curves
Solution:
Chainage of intersection point Minus TL
Chainage of T1
Plus L
Chainage of compound curvature (N) Plus LS
Chainage of T2
= 3415 m
= - 422.95 m
= 2992.05 m
= + 418.88 m
= 3410.93 m
= + 244.35 m
= 3655.25 m
Compound Curves

## Slide 9: Assignment No: 02
Q1): Two roads having a deviation angle of 45° at apex point V are to be joined by a 200 m radius circular curve. If the chainage of apex point is 1839.2 m, calculate necessary data to set the curve by:
(a) ordinates from long chord at 10 m interval. (b) method of bisection to get every eighth point on curve. (c) radial and perpendicular offsets from every full station of 30 m along tangent. (d) offsets from chord produced.
Q2): A circular curve of radius of 17.5 chains deflecting right through 32°40′, is to be set out between two straights having chainage of the point of intersection as (51 + 9.35). Calculate the necessary data to set out the curve by the method of deflection angles if length of one chain=20m.

## Slide 10: Exercise
Q3) Two straights AP and QC meet at an inaccessible point I. A circular curve of 500 m radius is to be set out joining the two straights. The following data were collected: ∠APQ = 157°22′, ∠CQP = 164°38′, PQ = 200 m.
Calculate the necessary data for setting out the curve by the method of offsets from long chord. The chain to be used is of 30 m length, and the chainage of P is (57 + 17.30) chains