## Slide 1: Lecture
HIGHWAY GEOMETRIC DESIGN: Horizontal allignment

## Slide 2: Design of Horizontal Alignment:
Various design elements to be considered in the horizontal alignment are :
a. Design speed
b. Horizontal curve
c. Super elevation
d. Widening of pavement on curves
e. Type and length of transition curves

## Slide 3: a. Design speed
The design speed is the main factor on which geometric design elements depends.
The design speed of roads depends upon
i) Class of the road
ii) Terrain

## Slide 4: Classification of Terrain

## Slide 5: Design Speed On highways

## Slide 6: b. Horizontal curve
A horizontal highway curve is a curve in plan to provide change in direction to the central line of a road.
When a vehicle traverses a horizontal curve, the centrifugal force acts horizontally outwards through the centre of gravity of the vehicle.
The centrifugal force is given by the equation:
P = Wv²∕gR

## Slide 7: b. Horizontal curve
where,
P=centrifugal force in kg
W=Weight of the vehicle in kg
R=radius of the circular curve in m
v=speed of the vehicle in m/s
g=acceleration due to gravity=9.8 m/s2

## Slide 8: b. Horizontal curve
P/W is known as the centrifugal ratio or the impact factor. The centrifugal ratio is thus equal to v²∕gR.
The centrifugal force acting on a vehicle negotiating a horizontal curve has two effects:
Tendency to overturn the vehicle outwards about the outer wheels
Tendency to skid the vehicle laterally, outwards

## Slide 9: i. Overturning effect:

## Slide 10: i. Overturning effect:
The equilibrium condition for overturning will occur when
Ph = Wb/2,
or when P/W =b/2h.
This means that there is danger of overturning when the centrifugal ratio P/W or v²/g R attains a values of b/2h.

## Slide 11: ii. Transverse skidding effect:

## Slide 12: ii. Transverse skidding effect:
The equilibrium condition for the transverse skid resistance developed is given by
P = FA+ FB
= f(RA+RB) =fW
Since P = f W, the centrifugal ratio P/W is equal to ‘f ‘. In other words when the centrifugal ratio attains a value equal to the coefficient of lateral friction there is a danger of lateral skidding.

## Slide 13: ii. Transverse skidding effect:
If ‘f’ is less than ‘b/2h’,the vehicle would skid and not overturn.
If ‘b/2h’ is lower than ‘f’, the vehicle would overturn on the outer side before skidding.
Thus the relative danger of lateral skidding and overturning depends on whether f is lower or higher than b/2h.

## Slide 14: c. Super elevation (e):
In order to counteract the effect of centrifugal force and to reduce the tendency of the vehicle to overturn or skid, the outer edge of the pavement is raised with respect to the inner edge, thus providing a transverse slope throughout the length of the horizontal curve.
This transverse inclination to the pavement surface is known as Super elevation or cant or banking.

## Slide 15: c. Super elevation (e):
The Super elevation ‘e’ is expressed as the ratio of the height of outer edge with respect to the horizontal width.

## Slide 16: c. Super elevation (e):

## Slide 17: Analysis of Super elevation:

## Slide 18: Analysis of Super elevation
For equilibrium condition,
P cosө=W sinө+FA+FB
P cosө=W sinө+ f.RA + f.RB
P cosө=W sinө+f(RA+RB)
P cosө=W sinө+f(W cos ө+P sin ө)
P(cosө – f sinө)=W sinө+f Wcosө
Dividing by Wcosө,
P/W(1- f tanө)=tanө+f
Centrifugal ratio =P/W= tanө+f /(1-f tanө)

## Slide 19: Analysis of Super elevation
The value of coefficient of lateral friction ‘f’ is taken as 0.15 and tanө i.e. super elevation seldom exceeds 7-10%.
Therefore,
Centrifugal ratio =P/W = tanө + f
P/W = e + f ……i
but P/W = v²∕gR ……ii
Therefore, the general equation for the design of super elevation is given by,
e + f = v²∕gR

## Slide 20: Analysis of Super elevation
If ‘V’ speed of the vehicle is in kmph,
e + f = V²∕ 127R
where,
e=rate of Superelevation = tanӨ
f = design value of lateral friction coefficient = 0.15
v = speed of the vehicle, m/sec
R = radius of the horizontal curve, m
g = acceleration due to gravity = 9.81 m/sec²

## Slide 21: Maximum Superelevation
Indian Roads Congress (IRC) has fixed the maximum limit of Superelevation in plain, rolling terrains and in snow bound areas as 7.0 %.
On hill roads not bound by snow a maximum Superelevation upto10% is recommended.
On urban road stretches with frequent intersections, it may be necessary to limit the maximum Superelevation to 4.0 %.

## Slide 22: Minimum Superelevation
From drainage consideration it is necessary to have a minimum cross slope to drain off the surface water.
If the calculated superelevation is equal to or less than the camber of the road surface, then the minimum superelevation to be provided on horizontal curve may be limited to the camber of the surface.

## Slide 23: Steps For Superelevation Design
Step-I:
The superelevation for 75 percent of design speed is calculated, neglecting the friction.
e =(0.75v)² ∕ gR …..if ‘v’ is in m/sec
e =(V)²∕ 225R …..if ‘V’ is in kmph
Step-II:
If the calculated value of ‘e’ is less than 7% or 0.07 the value so obtained is provided.
If the value of ‘e’ exceeds 7% or 0.07 then provides maximum superelevation equal to 7% or 0.07 and proceed with step-III or IV.

## Slide 24: Steps For Superelevation Design
Step-III:
Check the coefficient of friction developed for the maximum value of e =0.07 at the full value of design speed.
f =v²∕ gR - 0.07 …..if ‘v’ is in m/sec
f =V²∕ 127R - 0.07 …..if ‘V’ is in kmph
If the value of ‘f’ thus calculated is less than 0.15, the super elevation of 0.07 is safe for the design speed.
If not, calculate the restricted speed as given in Step -IV.

## Slide 25: Steps For Superelevation Design
Step-IV:
The allowable speed at the curve is calculated by considering the design coefficient of lateral friction and the maximum superelevation.
e + f =0.07+0.15=va²∕ gR=Va²∕ 127R
e + f =0.22=va²∕ gR = Va²∕ 127R
Safe allowable speed (va or Va) is calculated as:

## Slide 26: Steps For Superelevation Design
If the allowed speed, as calculated above is higher than the design speed, then the design is adequate and provides a superelevation of ‘e’ equal to 0.07.
If the allowable speed is less than the design speed, the speed is limited to the allowed speed calculated above and appropriate warning sign and speed limit regulation sign are installed to restrict and regulate the speed.

## Slide 27: Radius of Horizontal Curve:
e + f = v²∕gR = V²∕ 127R
If maximum Allowable superelevation rate has been fixed as 7% and lateral friction f is 0.15 then,
0.07 + 0.15 = v²∕gR = V²∕ 127R
0.22= v²∕gR = V²∕ 127R
If design speed is decided ruling and minimum radius is calculated as,
Rruling = v²∕g(e + f) = V²∕ 127(e + f)
Rmin = v’²∕g(e + f) = V’²∕ 127(e + f)

## Slide 28: Radius of Horizontal Curve:
where,
e=rate of Superelevation
f = design value of lateral friction coefficient = 0.15
v or V= design speed of the vehicle, m/sec or kmph
v’ or V’= minimum design speed of the vehicle, m/sec or kmph
g = acceleration due to gravity = 9.81 m/sec²

## Slide 29: d. Widening of pavement on horizontal curves:
On horizontal curves, especially when they are Less than 300m radii, it is common to widen the pavement slightly more than the normal width.
Widening is needed for the following reasons:
a. An automobile has a rigid wheel base and only the front wheels can be turned, when this vehicle takes a turn to negotiate a horizontal curve, the rear wheel do not follow the same path as that of the front wheels. This phenomenon is called off tracking.

## Slide 30: d. Widening of pavement on horizontal curves:
b. While two vehicle cross or overtake at horizontal curve there is psychological tendency to maintain a greater clearance between the vehicle for safety.
c. For greater visibility at curve, the driver have tendency not to follow the central path of the lane, but to use the outer side at the beginning of the curve.
d. At higher speed superelevation and lateral friction cannot counteract centrifugal force and skidding may occur.

## Slide 31: Analysis of extra widening on horizontal curves:
The extra widening of pavement on horizontal curves is divided into two parts:
a. Mechanical widening/Off tracking
b. Psychological widening

## Slide 32: a. Mechanical widening/Off tracking (Wm):

## Slide 33: a. Mechanical widening/Off tracking (Wm):
Consider
OA=R1=radius of the path traversed by the outer rear wheel,m
OB=R2=radius of the path traversed by the outer front wheel,m
Wm=mechanical widening due to off-tracking, m
l=length of wheel base,m
R=mean radius of the horizontal curve, m
OB-OA= R2 - R1 =Wm

## Slide 34: a. Mechanical widening/Off tracking (Wm):

## Slide 35: b. Psychological widening (Wps):
An empirical formula has been recommended by IRC for deciding the additional psychological widening.
The psychological widening is given by the formula:

## Slide 36: b. Psychological widening (Wps):
The total extra widening is given by,
We=Wm + Wps
where,
n=no. of traffic lanes
l = length of wheel base =6.1 or 6 m
V=design speed, kmph
R = radius of the horizontal curve, m

## Slide 37: e. Horizontal Transition Curve:
A transition curve has a radius which decreases from infinity at the tangent point to a designed radius of the circular curve.
The rate of change of radius of the transition curve will depend on the shape of the curve adopted and the equation of the curve.

## Slide 38: e. Horizontal Transition Curve:

## Slide 39: Objectives of providing transition curve:
A transition curve which is introduced between straight and a circular curve will help in:
a. Gradually introducing centrifugal force.
b. Gradually introducing designed superelevation.
c. Gradually introducing extra widening.
d. To enable the driver turn steering gradually for his own comfort and safety.