## Slide 1: Electrical Transmission System
In last lecture we have discussed about Three-Phase Short Transmission Lines, Effect of Load p.f. on Regulation and Efficiency. In this lecture we will study about some Effects on transmission lines such as, Heat in the system, proximity effect and Ferranti effect.

## Slide 3: Effects on Transmission Line Heat in the system
 Heat in the wire decreases the efficiency of the distribution system. It also creates a fire hazard. Contraction and expansion of wire due to cooling and heating of wire loosens wire connections. This makes it possible for the electricity to arc and the heat output can reach 1800 degrees Fahrenheit. This is enough heat to ignite wood or insulation.
 Skin effect and proximity effect are the two major sources of heat in wire.

## Slide 4: Heat in the system
 Reducing heat in the electrical system is critical to improving power quality. Wire is the heart of the electrical distribution system. A typical facility can have tens of thousands of feet of wire throughout the facility and wire is a major source of heat. Heat prematurely degrades wire quality causing both energy losses and burnout of the wire.
 The resistance in an electrical system is never constant. It depends on various factors such as humidity, length of wire and high frequency noise. Wire is the main conduit of electricity and is central to the electrical system. Resistance in the wire converts a portion of electrical energy into heat.

## Slide 5: Proximity Effect
 Along with skin effect, proximity effect is a common problem found in every electrical system. Proximity effect is defined as the jumping magnetic field from one conductor to another conductor nearby. The major causes of proximity effect are closeness of the wires, bends in the wire, skin effect and high frequency noise.
 The term proximity effect refers to the influence of alternating current in conductor on the current distribution in another, nearby conductor.

## Slide 6: Proximity Effect
 Qualitatively, it can also be explained by Lentz's law Consider a coaxial cable of finite Assume for the moment that there a alternating current only in the inner conductor(for example, that it is connected to generator), and that the outer conductor connected to anything. outer conductor is much than the skin depth, there is practically no magnetic field conductor.

## Slide 7: Proximity Effect
 If we apply Ampere's law a coaxial circular contour contained in that conductor, it follows that the induced current on the inside surface of the outer conductor is exactly equal and opposite to the current in the inner conductor. is an example of the proximity effect. he current from the inner surface of the outer conductor must close into itself over the outer conductor, so that on that surface the same current exists as in the inner conductor.

## Slide 8: Ferranti Effect
 A long transmission line draws a substantial quantity of charging current. If such a line is open circuited or very lightly loaded at the receiving end, the voltage at receiving end may become greater than voltage at sending end. This is known as Ferranti Effect and is due to the voltage drop across the line inductance (due to charging current) being in phase with the sending end voltages. Therefore both capacitance and inductance is responsible to produce this phenomenon

## Slide 9: Ferranti Effect
 The capacitance (and charging current) is negligible in short line but significant in medium line and appreciable in long line. Therefore this phenomenon occurs in medium and long lines.
 Represent line by equivalent -model

## Slide 10: Ferranti Effect
 Line capacitance is assumed to be concentrated at the receiving end.
OM = receiving end voltage Vr
OC = Current drawn by capacitance = Ic
MN = Resistance drop
NP = Inductive reactance drop Therefore;
OP = Sending end voltage at no load and is less than receiving end voltage (Vr)

## Slide 11: Ferranti Effect
 Since, resistance is small compared to reactance; resistance can be neglected in calculating Ferranti effect.
Ic  YVr....... ....... ........ ........ ........ ........ ......1
Vs  Vr  ZIc
Vs  Vr  R  jω LIc
Here Resistanceis verysmall or negligiable So, R  0
Vs  Vr  0  jω LIc
Vs  Vr  jω L Ic...... ........ ........ ........ ........ .2

## Slide 12: Ferranti Effect
 Receiving end voltage is greater than sending end voltage and this effect is called Ferranti Effect. It is valid for open circuit condition of long line.
Vr - Vs  Vr -[Vr  jω L Ic]
 Vr - Vr  jω L Ic
  jω L Ic
  jω L{YVr}
  jω L{Jω C}Vr
2
 ω^2 LCVr
2
As Vr  Vs is Positive their is some voltage rise.

## Slide 13: References
1. V. K. Mehta and Rohit Mehta [Principles of Power
System] published by S. Chand.
1. D. M. Patel [Electrical Power System -1] published by Atul Prakashan.