## Slide 1: Mobile Computing
Cellular Networks

## Slide 2: Public Switched Telephone Network - PSTN
Local
switch
Local
switch
Transit
switch
Outgoing
call
Incoming
call
Transit
switch
Transit
switch
Long distance network
- Transfer mode: circuit switching
- All the network (except part of the access network) is digital
- Each voice channel is usually 64kb/s

## Slide 3: Basic Call
Calling terminal
Network
Called terminal
Off-hook
Dial tone
Dialing
Ring indication
Alert signal
Off hook
Remove ring indication
Bi-directional channel
On hook
Billing
On hook signal
Resource allocation
Translation + routing
Conversation

## Slide 4: Next Up: Wireless Communications
Fundamental aspects of wireless networks and radio communications

## Slide 5: Frequencies for Communication
VLF = Very Low Frequency UHF = Ultra High Frequency
LF = Low Frequency SHF = Super High Frequency
MF = Medium Frequency EHF = Extremely High Frequency
HF = High Frequency UV = Ultraviolet Light
VHF = Very High Frequency
Frequency and wave length
   = c/f
  wave length , speed of light c  3x108m/s, frequency f
1 Mm
300 Hz
10 km
30 kHz
100 m
3 MHz
1 m
300 MHz
10 mm
30 GHz
100 m
3 THz
1 m
300 THz
visible light
VLF
LF
MF
HF
VHF
UHF
SHF
EHF
infrared
UV
optical transmission
coax cable
twisted pair

## Slide 6: Frequencies for Mobile Communication
Low Frequencies:
  low data rates
  travel long distances
  follow Earth’s surface
  penetrate objects and water (submarine communication)
High Frequencies:
  high data rates
  short distances
  straight lines
  cannot penetrate objects (“Line of Sight” or LOS)

## Slide 7: Frequencies and Regulations
ITU-R holds auctions for new frequencies, manages frequency bands worldwide (WRC, World Radio Conferences)
Examples | Europe | USA | Japan
Cellular phones | GSM 880-915, 925-960, 1710-1785, 1805-1880 UMTS 1920-1980, 2110-2170 | AMPS, TDMA, CDMA, GSM 824-849, 869-894 TDMA, CDMA, GSM, UMTS 1850-1910, 1930-1990 | PDC, FOMA 810-888, 893-958 PDC 1429-1453, 1477-1501 FOMA 1920-1980, 2110-2170
Cordless phones | CT1+ 885-887, 930-932 CT2 864-868 DECT 1880-1900 | PACS 1850-1910, 1930-1990 PACS-UB 1910-1930 | PHS 1895-1918 JCT 245-380
Wireless LANs | 802.11b/g 2412-2472 | 802.11b/g 2412-2462 | 802.11b 2412-2484 802.11g 2412-2472
Other RF systems | 27, 128, 418, 433, 868 | 315, 915 | 426, 868

## Slide 8: Signal propagation ranges
Transmission range
  communication possible
  low error rate
Detection range
  detection of the signal possible
  no communication possible
Interference range
  signal may not be detected
  signal adds to the background noise
distance
sender
transmission
detection
interference

## Slide 9: Cellular Network Basics
Cellular network/telephony is a radio-based technology; radio waves are electromagnetic waves that antennas propagate
Most signals are in the 850 MHz, 900 MHz, 1800 MHz, and 1900 MHz frequency bands
Cell phones operate in this frequency range (note the logarithmic scale)

## Slide 10: Cellular Network
Base stations transmit to and receive from mobile devices at the assigned spectrum
  Multiple base stations use the same spectrum (spectral reuse)
The service area of each base station is called a cell
Each mobile terminal is typically served by the ‘closest’ base stations
  Handoff when terminals move

## Slide 11: Architecture of Cellular Networks
External
Network
Cellular Network
Mobile Station
Base Station
Mobile Switching Center (MSC)
Server (e.g., Home Location Register)

## Slide 13: Registration
Tune on the strongest signal
Nr: 079/4154678

## Slide 14: Service Request
079/4154678
079/8132627
079/4154678
079/8132627

## Slide 15: Paging Broadcast
079/8132627?
079/8132627?
079/8132627?
079/8132627?
Note: paging makes sense only over a small area

## Slide 16: Response
079/8132627
079/8132627

## Slide 17: Channel Assignment
Channel
47
Channel
47
Channel
68
Channel
68

## Slide 18: Conversation

## Slide 19: Handoff (or Handover)

## Slide 20: Message Sequence Chart
Caller
Base
Station
Switch
Base
Station
Callee
Periodic registration
Periodic registration
Service request
Service request
Ring indication
Ring indication
Page request
Page request
Paging broadcast
Paging broadcast
Paging response
Paging response
Assign Ch. 47
Tune to Ch.47
Assign Ch. 68
Tune to Ch. 68
Alert tone
User response
User response
Stop ring indication
Stop ring indication

## Slide 21: Cellular Network Generations
It is useful to think of a cellular network in terms of generations:
  0G: Briefcase-size mobile radio telephones
  1G: Analog cellular telephony
  2G: Digital cellular telephony
  3G: High-speed digital cellular telephony (including video telephony)
  4G: IP-based “anytime, anywhere” voice, data, and multimedia telephony at faster data rates than 3G (being deployed now)

## Slide 22: Evolution of Cellular Networks
1G
2G
3G
4G
2.5G

## Slide 23: The Multiple Access Problem
The base stations need to serve many mobile terminals at the same time (both downlink and uplink)
All mobiles in the cell need to transmit to the base station
Interference among different senders and receivers
So we need multiple access scheme

## Slide 24: Multiple Access Schemes
Frequency Division Multiple Access (FDMA)
Time Division Multiple Access (TDMA)
Code Division Multiple Access (CDMA)
3 orthogonal schemes:

## Slide 25: Frequency Division Multiple Access
Each mobile is assigned a separate frequency channel for the duration of the call
Sufficient guard band is required to prevent adjacent channel interference
Usually, mobile terminals will have one downlink frequency band and one uplink frequency band
Different cellular network protocols use different frequencies
Frequency is a precious and scarce resource
  Cognitive radio research
frequency

## Slide 26: Time Division Multiple Access
Time is divided into slots and only one mobile terminal transmits during each slot
Each user is given a specific slot. No competition in cellular network
  Unlike Carrier Sensing Multiple Access (CSMA) in Wi-Fi
Guard time – signals transmitted by mobile terminals at different locations do not arrive at the base station at the same time