## Slide 1: Module # 1 Introduction To Advanced Design of Reinforced Concrete Structures

## Slide 2: Historical Development of Cement and Reinforced Concrete

## Slide 3: Historical Development of Cement and Reinforced Concrete
Cement
  In 1824 Joseph Aspdin mixed limestone and clay and heated them in a kiln to produce cement.
  The commercial production started around 1880.
Reinforced Concrete
  Joseph Monier, owner of a French nursery garden began experimenting (in around 1850) on reinforced concrete tubs with iron for planting trees.
  The first RC building in the US was a house built in 1875 by W. E. Ward, a mechanical engineer.

## Slide 4: Building Codes and the ACI Code
General Building Codes
  Cover all aspects of building design and construction from architecture to structural to mechanical and electrical---. UBC (Uniform Building Code), IBC (International Building Code) and Euro-code are general building codes.
Seismic Codes
  Cover only seismic provisions of buildings such as SEAOC (Structural Engineers Association of California) and NEHRP (National Earthquake Hazards Reduction Program) of USA, BCP-SP 07 (Building code of Pakistan- Seismic Provision) of Pakistan.
  Material Specific Codes
  Cover design and construction of structures using a specific material or type of structure such as ACI (American concrete Institute), AISC (American Institute of Steel Construction) , AASHTO (American Association of State Highway and Transportation Officials) etc.
Others such as ASCE
  Cover minimum design load requirement, Minimum Design Loads for Buildings and other Structures (ASCE7-10).

## Slide 5: Building Codes and the ACI Code
General Building Codes in USA
  The National Building Code (NBC) : Published by the Building Officials and Code Administrators International was used primarily in the northeastern states.
  The Standard Building Code (SBC): Published by the Southern Building Code Congress International was used primarily in the southeastern states.
  The Uniform Building Code (UBC): Published by the International Conference of Building Officials, was used mainly in the central and western United States.
  The International Building Code IBC,
    Published by International Code Council ICC for the first time in 2000, revised every three years.
    The IBC has been developed to form a agreement single code for USA.
    Currently IBC 2015 is available.
    UBC 97 is the last UBC (Uniform Building Code) and is still existing but will not be updated. Similarly NBC, SBC will also be not updated.
  Building Code of Pakistan
    Seismic Provision BCP SP-07 (Building code of Pakistan- Seismic Provision) has adopted the seismic provisions of UBC 97 for seismic design of buildings.
    IBC 2000 could not be adopted because some basic input data required by IBC for seismic design does not exist in Pakistan.

## Slide 6: Building Codes and the ACI Code
Seismic Codes in USA
  NEHRP (National Earthquake Hazards Reduction Program) Recommended Provisions for the Development of Seismic Regulations for New Buildings developed by FEMA (Federal Emergency Management Agency).
  The NBC, SBC and IBC have adopted NEHRP for seismic design.
  “Blue Book Structural Engineers Association of California”, has its seismic provisions based on the Recommended Lateral Force Requirements (the SEAOC “Blue Book”) published by the Seismology Committee of SEAOC (Structural Engineers Association of California).

## Slide 7: Building Codes and the ACI Code
The ACI MCP (American Concrete Institute Manual of Concrete Practice)
  ACI MCP contains 150 ACI committee reports; revised every three years.
    ACI 318: Building Code Requirements for Structural Concrete.
    ACI 315: The ACI Detailing Manual.
    ACI 349: Code Requirement for Nuclear Safety Related Concrete Structures.
    Many others.

## Slide 8: Building Codes and the ACI Code
The ACI 318 Code
  The American Concrete Institute “Building Code Requirements for Structural Concrete (ACI 318)” referred to as the ACI code.
  It provides minimum requirements for structural concrete design or construction.
  The term “structural concrete” is used to refer to all plain or reinforced concrete used for structural purposes.
  Pre-stressed concrete is included under the definition of reinforced concrete.
Legal Status of The ACI 318 Code
  The ACI 318 code has no legal status unless adopted by a state or local jurisdiction.
  It is also recognized that when the ACI code is made part of a legally adopted general building code, that general building code may modify some provisions of ACI 318 to reflect local conditions and requirements.

## Slide 9: Building Codes and the ACI Code
The Compatibility Issue in BCP SP-2007
  Building Code of Pakistan, Seismic Provision BCP SP-07 has adopted the seismic provisions of UBC 97 for seismic design of buildings.
  As the UBC 97 has reproduced ACI 318-95, the load combinations and strength reduction factors of ACI 318-02 and later codes are not compatible with UBC 97 and hence BCP SP-07. Therefore ACI 318-02 and later codes cannot be used directly for design of a system analyzed according to the seismic provisions of UBC 97.
  To resolve this issue, BCP SP-2007 recommends using ACI 318-05 code for design except that load combinations and strength reduction factors are to be used as per UBC 97.
  The IBC adopts the latest ACI code by reference whenever it is revised and hence are fully compatible.

## Slide 10: The Design and Design Team

## Slide 11: The Design and Design Team
What is a Structural Design?
Process of determining reliable structural system, selection of suitable materials and determination of optimum member sizes for the structure to be built.
Aim is ensure that the structure will perform satisfactorily during its design life

## Slide 12: The Design and Design Team
General:
  The design covers all aspects of structure, not only the structural design.
  The structural engineer is a member of a team whose members work together to design a building, bridge, or other structure.
Relationship between Engineer and Architect
  Close cooperation with the architect in the early stages of a project is essential in developing a structure that not only meets the functional and aesthetic requirements but achievement to the fullest the special advantages of reinforced concrete.

## Slide 13: The Design and Design Team
  Four Major Objectives of Design
  1. Fitness for purpose (Appropriateness):
Arrangement of spaces, spans, ceiling height, access and traffic flow must complement the intended use.
The structure should fit its environment and be aesthetically pleasing
2. Economy
• Overall cost of structure should not exceed the client’s budget
• Designer should take into account: cost of materials, build ability, construction time, cost of temporary structures and maintenance costs
3. Structural Adequacy (safety)
• Structure must be strong to safely support all anticipated loadings
• Structure must not deflect, overturn, tilt, vibrate or crack in a manner that impairs its usefulness
4. Maintainability
The structure should be simple so that it is maintained easily

## Slide 14: Structural Elements

## Slide 15: Structural Elements
• Beams: horizontal members carrying lateral loads
• Slabs: horizontal plate elements carrying lateral loads
• Columns: vertical members carrying primarily axial loads but generally subjected to axial load and moment
• Walls: vertical plate elements resisting vertical, lateral or in-plane loads
• Foundations: pads or strips supported directly on the ground that spread loads from columns or walls to the ground
• Stairs: plate elements consists of a flight of steps, usually with one or more landings provided between the floor levels

## Slide 16: Structural Elements

## Slide 17: Code of Practice

## Slide 18: Code of Practice
Document that gives recommendations for the design and construction of structures
Contains detailed requirements regarding loads, stresses, strengths, design formulas and methods of achieving the required performance of complete structure.
Code of Practice functions
Ensure adequate structural safety
Simplify the task of designer
Codes ensure a measure of consistency among different designers
Have legal validity, in that they protect the structural designers from any legal responsibility due to structural failures that are caused by inadequate supervision, faulty material and construction

## Slide 19: Concrete Structural Systems

## Slide 20: Concrete Structural Systems
Selection Criterion
  Depending on structural spans, loading conditions, purpose of building, availability of formwork, skilled labor and material etc., a number of different structural systems such as flat plate, flat slab, one-way or two way joist system etc. are possible.
  Flat Plate
A flat plate is a slab floor system in which the slab of uniform thickness is supported directly on columns.
Flat plates are economical for:
  Short and medium spans
  Economical range: 15 ft – 25 ft, and
  Moderate live loads
Punching shear is a typical problem in flat plates.
Beamless systems with drop panels or column capitals or both are termed as flat slab systems.
Short and medium spans, economical range 20 ft. – 30 ft.
    Drop Panel: Thick part of slab in the vicinity of columns
    Column Capital: Column head of increased size

## Slide 21: Concrete Structural Systems
Beam-Supported Slab
  In beam supported slab, the perimeter beams are usually concrete cast monolithically with the slab, although they may also be structural steel, often encased in concrete for composite action and for improved fire resistance.
  Suitable for long spans and for parking structures.
  Specially for intermediate and heavy loads for span up to about 30 ft.

## Slide 22: Concrete Structural Systems
Beam-and-Girder Floors
  A beam and girder floor consists of a series of parallel beams supported at their extremities by girders, which in turn frame into concrete columns placed at more or less regular intervals over entire floor area.
  Adapted to any loads and spans. Normal range in column spacing is from 16 to 32 ft.

## Slide 23: Concrete Structural Systems
Banded-slab System
  For light loads, a floor system has been developed in which the beams are omitted in one direction, the one-way slab being carried directly by column line beams that are very broad and shallow.
  These beams, supported directly by the columns, become little more than a thickened portion of the slab. This type of construction is known as banded slab construction.
One-Way Joist
  A one-way joist construction consists of a monolithic
  combination of regularly spaced ribs and a top slab
  (T beam or Joist) arranged to span in one direction.
  Long spans, economic range: 30 ft. – 50 ft.

## Slide 24: Concrete Structural Systems
Two-Way Joist
  A two-way joist system, or waffle slab, comprises evenly spaced concrete joists spanning in both directions and a reinforced concrete slab cast integrally with the joists.
  Like one-way joist system, a two way system will be called as two- way joist system if clear spacing between ribs (dome width) does not exceed 30 inches.

## Slide 25: Concrete Structural Systems
Composite Construction with Steel Beams
  In this system, columns, beams, and girders consist of structural steel whereas the floors are reinforced concrete slabs.
  The spacing of beams is usually 6 to 8 ft.

## Slide 26: Concrete Structural Systems
Steel Deck Reinforced Concrete Slab
  In this structural system, the steel deck serves as stay in place form and, with suitable detailing the slab becomes composite with the steel deck, serving as the main tensile flexural steel.
  The spacing of beams is usually 12 ft.

## Slide 27: Concrete Structural Systems
Post-Tension Slab
  In the post-tensioned slab systems, hollow ducts are provided in slab through which the tendons are placed. Tendons are tensioned after the concrete has gained its strength. Columns and beams are regular reinforced concrete members.
  Longer spans can be achieved due to pre-stress, which can be used to counteract deflections.

## Slide 28: Limit State and the Design of Reinforced Concrete

## Slide 29: Limit State and the Design of Reinforced Concrete
Limit State
  State of a structure which represents the acceptable limit of an aspect of structural behavior.
  Criterion for safe design is the structure should not become unfit for use – not reach a limit state during its intended life
The three limit states
Ultimate Limit States
Serviceability Limit States
Special Limit States

## Slide 30: Limit State and the Design of Reinforced Concrete
1. Ultimate Limit States.
  These involve a structural collapse of part or all of the structure.
  Such a limit state should have a very low probability of occurrence, since it may lead to loss of life and major financial losses.
  Deals with the strength and stability of the structure under the maximum design load it is expected to carry.
  No part or whole of the structure should collapse, overturn or buckle under any combination of design load
The Major Ultimate limit States are
Divided into the following categories
• EQU – Loss of equilibrium of the structure
• STR – Internal failure or excessive deformation of the structure or structural members
• GEO – failure due to excessive deformation of the ground
• FAT – fatigue failure of the structure or structural members (Fatigue is the weakening of a material caused by cyclic loading that results in progressive and localized structural damage and the growth of cracks.)

## Slide 31: Limit State and the Design of Reinforced Concrete
2. Serviceability Limit States
  These involve disruption of the functional use of the structure, but not collapse.
  Since there is less danger of loss of life.
The Serviceability Limit States are
  1. Excessive deflections
  2. Excessive crack widths
  3. Undesirable vibrations

## Slide 32: Limit State and the Design of Reinforced Concrete
3. Special Limit States
  This class of limit state involves damage or failure due to abnormal conditions or abnormal loadings.
Special Limit States include
  1. Damage or collapse in extreme earthquakes.
  2. Structural effects of fire, explosions, or vehicular accidents.

## Slide 33: Limit State and the Design of Reinforced Concrete
Limit State Design of RC Buildings
  1. RC buildings are designed for Ultimate Limit States
  2. Subsequently checked for Serviceability Limit States
  3. Under special condition also checked for Special Limit States

## Slide 34: Basic Design Relationship

## Slide 35: Basic Design Relationship
The Capacity and Demand
  Capacity must be ≥ Demand (in same units)
  Demand: An imposed action on structure (Loads)
  Capacity: The overall resistance of structure (Strength)
  Load Effects: Bending, torsion, shear, axial forces, deflection, vibration
Working Stress Design approach
  1. Demand is kept the same or increased
  2. Capacity is reduced by half or factored (Will be discussed in loads combination)

## Slide 36: Basic Design Relationship
Limit State Design approach
  Capacity is reduced and demand is increased based on scientific justification.
  In LSD approach, we have
    f Mn ≥ Mu (α M )
    f Vn ≥ Vu (α V )
    f Pn ≥ Pu (α P )
    f Tn ≥ Tu (α T )
      f = strength reduction factor
      α = load amplification factor

## Slide 37: Design Procedure of the ACI Code

## Slide 38: Design Procedure of the ACI Code
4.6.2- Structural members shall have design strength for all sections (greater than or equal to the required strength) calculated for the factored loads or loads in combinations as required by this Code or the general building code.
4.6.1- Design strength of a member and its joints and connections, in terms of moment, axial force, shear, torsion, and bearing, shall be taken as the nominal strength Sn multiplied by the applicable strength reduction factor ϕ.
This process is called strength design in the ACI code.

## Slide 39: Design Procedure of the ACI Code
In the AISC (American Institute of Steel Construction) Specifications for steel design, the same design process is known as LRFD (Load and Resistance Factor Design).
Strength design and LRFD are methods of limit-state design.
Primary attention is always placed on the ultimate limit states, with the serviceability limit states being checked after the original design is completed.

## Slide 40: Design Loads in the ACI Code

## Slide 41: Design Loads in the ACI Code
ACI 318-14, Section 5.2 (LOADING):
5.2.1: Loads shall include self-weight; applied loads; and effects of pre-stressing, earthquake, control of volume change, and differential settlement.
Section R5.2.1: Provisions in the Code are associated with dead, live, wind, and earthquake loads such as those recommended in ASCE/SEI 7.
SEI = Structural Engineering Institute
ASCE = American Society of Civil Engineers

## Slide 42: Design Loads in the ACI Code
ASCE Recommendations on Loads:
  ASCE 7-10 sections 1 to 10 are related to design loads for buildings and other structures.
  The sections are named as: general, combinations of loads, (dead loads, soil loads and hydrostatic pressure), live, flood, snow, rain and ice loads.
Loads on Structure During Construction
During the construction of concrete buildings, the weight of the fresh concrete is supported by formwork, which frequently rests on floors lower down in the structure.
ACI section 26.11.2.1(c) states the following:
  No construction loads shall be placed on, nor any formwork removed from, any part of the structure under construction except when that portion of the structure in combination with remaining formwork has sufficient strength to support safely its weight and loads placed there on.

## Slide 43: Load Combinations of ACI and UBC

## Slide 44: Load Combinations of ACI and UBC
Section 5.3 of ACI 318-14 code
1.4D
1.2D + 1.6L
1.2D + 1.0E + 1.0L
0.9D + 1.0E
Section 1928.1.2.3 of UBC code
1.4D
1.4D + 1.7L
1.2D + 1.5E + 0.5L
0.9D + 1.5E
Load Types
Dead = D, Live = L, Seismic = E

## Slide 45: Strength Reduction Factors Of ACI and UBC

## Slide 46: Strength Reduction Factors Of ACI and UBC
Strength Reduction Factors | ACI 318-14 Code, Section 21.2 f | UBC 1909.3.2 f
Tension-controlled | 0.90 | 0.90
Shear and torsion | 0.75 | 0.85
Compression-controlled (spiral) | 0.70 | 0.75
Compression-controlled (other) | 0.65 | 0.70
Bearing | 0.65 | 0.70

## Slide 47: Customary Dimensions and Construction Tolerance

## Slide 48: Customary Dimensions
The actual as-built dimensions will differ slightly from those shown on the drawings, due to construction inaccuracies.
ACI Committee 117 has published a comprehensive list of tolerance for concrete construction and materials.
As an example, tolerances for footings are 2 inches and ½ inch on plan dimensions and 5 percent of the specified thickness.

## Slide 49: Concrete and Reinforced Concrete

## Slide 50: Concrete and Reinforced Concrete
Concrete is a mixture of sand, gravel, crushed rock, or other aggregates held together in a rocklike mass with a paste of cement and water.
Sometimes one or more admixtures are added to change certain characteristics of the concrete such as its workability, durability, and time of hardening.
As with most rocklike substances, concrete has a high compressive strength and a very low tensile strength.
Reinforced concrete is a combination of concrete and steel wherein the steel reinforcement provides the tensile strength lacking in the concrete.
Steel reinforcing is also capable of resisting compression forces as used in columns.

## Slide 51: Advantages of Reinforced Concrete as a Structural Material

## Slide 52: Advantages of Reinforced Concrete as a Structural Material
Reinforced concrete may be the most important material available for construction. It is used in one form or another for almost all structures, great or small—buildings, bridges, pavements, dams, retaining walls, tunnels, drainage and irrigation facilities, tanks, and so on.
The tremendous success of this universal construction material can be understood quite easily if its numerous advantages are considered. These include the following:
1. It has considerable compressive strength per unit cost compared with most other materials.
2. Reinforced concrete has great resistance to the actions of fire and water and, in fact, is the best structural material available for situations where water is present. During fires of average intensity, members with a satisfactory cover of concrete over the reinforcing bars suffer only surface damage without failure.
3. Reinforced concrete structures are very rigid.
4. It is a low-maintenance material.

## Slide 53: Advantages of Reinforced Concrete as a Structural Material
5. As compared with other materials, it has a very long service life. Under proper conditions, reinforced concrete structures can be used indefinitely without reduction of their load carrying abilities. This can be explained by the fact that the strength of concrete does not decrease with time but actually increases over a very long period, measured in years, because of the lengthy process of the solidification of the cement paste.
6. It is usually the only economical material available for footings, floor slabs, basement walls, piers, and similar applications.
7. A special feature of concrete is its ability to be cast into an extraordinary variety of shapes from simple slabs, beams, and columns to great arches and shells.
8. A lower grade of skilled labor is required for erection as compared with other materials such as structural steel.

## Slide 54: Disadvantages of Reinforced Concrete as a Structural Material

## Slide 55: Disadvantages of Reinforced Concrete as a Structural Material
To use concrete successfully, the designer must be completely familiar with its weak points as well as its strong ones. Among its disadvantages are the following:
1. Concrete has a very low tensile strength, requiring the use of tensile reinforcing.
2. Forms are required to hold the concrete in place until it hardens sufficiently. In addition, false work or shoring may be necessary to keep the forms in place for roofs, walls, floors, and similar structures until the concrete members gain sufficient strength to support themselves. Formwork is very expensive. In the United States, its costs run from one-third to two-thirds of the total cost of a reinforced concrete structure, with average values of about 50%. It should be obvious that when efforts are made to improve the economy of reinforced concrete structures, the major emphasis is on reducing formwork costs.

## Slide 56: Disadvantages of Reinforced Concrete as a Structural Material
3. The low strength per unit of weight of concrete leads to heavy members. This becomes an increasingly important matter for long-span structures, where concrete’s large dead weight has a great effect on bending moments. Lightweight aggregates can be used to reduce concrete weight, but the cost of the concrete is increased.
4. Similarly, the low strength per unit of volume of concrete means members will be relatively large, an important consideration for tall buildings and long-span structures.
5. The properties of concrete vary widely because of variations in its proportioning and mixing. Furthermore, the placing and curing of concrete is not as carefully controlled.

## Slide 57: Comparison of Reinforced Concrete and Structural Steel for Buildings and Bridges

## Slide 58: Comparison of Reinforced Concrete and Structural Steel for Buildings and Bridges
When a particular type of structure is being considered, the student may be puzzled by the question, “Should reinforced concrete or structural steel be used?”
There is much joking on this point, with the supporters of reinforced concrete referring to steel as that material that rusts and those favoring structural steel referring to concrete as the material that, when overstressed, tends to return to its natural state that is, sand and gravel.
There is no simple answer to this question, in as much as both of these materials have many excellent characteristics that can be utilized successfully for so many types of structures. In fact, they are often used together in the same structures with wonderful results.

## Slide 59: Comparison of Reinforced Concrete and Structural Steel for Buildings and Bridges
The selection of the structural material to be used for a particular building depends on the height and span of the structure, the material market, foundation conditions, local building codes, and architectural considerations.

## Slide 60: Comparison of Reinforced Concrete and Structural Steel for Buildings and Bridges
Foundation conditions can often affect the selection of the material to be used for the structural frame. If foundation conditions are poor, using a lighter structural steel frame may be desirable.
The building code in a particular city may favor one material over the other. For instance, many cities have fire zones in which only fireproof structures can be erected—a very favorable situation for reinforced concrete.
Finally, the time element favors structural steel frames, as they can be erected more quickly than reinforced concrete ones.
The time advantage, however, is not as great as it might seem at first because, if the structure is to have any type of fire rating, the builder will have to cover the steel with some kind of fireproofing material after it is erected.
In general, concrete is an excellent compression material and normally will be favored for short-span bridges and for cases where rigidity is required

## Slide 61: Compatibility of Concrete and Steel

## Slide 62: Compatibility of Concrete and Steel
Concrete and steel reinforcing work together beautifully in reinforced concrete structures.
The advantages of each material seem to compensate for the disadvantages of the other.
For instance, the great shortcoming of concrete is its lack of tensile strength, but tensile strength is one of the great advantages of steel.
Reinforcing bars have tensile strengths equal to approximately 100 times that of the usual concretes used.
The two materials bond together very well so there is little chance of slippage between the two; thus, they will act together as a unit in resisting forces.
The excellent bond obtained is the result of the chemical adhesion between the two materials, the natural roughness of the bars, and the closely spaced rib-shaped deformations rolled onto the bars’ surfaces.

## Slide 63: Compatibility of Concrete and Steel
Reinforcing bars are subject to corrosion, but the concrete surrounding them provides them with excellent protection.
The strength of exposed steel subjected to the temperatures reached in fires of ordinary intensity is nil, but enclosing the reinforcing steel in concrete produces very satisfactory fire ratings.

## Slide 64: Thanks