## Slide 1: PRINCIPLES OF USE OF PERSONAL PROTECTIVE EQUIPMENTS (PPE)

## Slide 2: What is PPE?
Personal Protective Equipment (PPE)
PPE is a precautionary step to protect yourself and the people around you.
PPE is specialized clothing or equipment worn for protection against dangerous or infectious materials.
PPE prevents contact with an infectious agent by creating a barrier between the potentially infectious material and the public health practitioner.

## Slide 3: Purpose of PPE
Public health practitioners should wear PPE to:
Stop the spread of illness/infection
Protect their health
Protect their client's health
Protect their family's health
Protect the community's health

## Slide 4: PPE available
Gowns, aprons, coveralls
Shoe covers
Hair covers
Respirators/Masks
Goggles or Face shields
Gloves

## Slide 5: PPE Gadgets
Masks
There are several types of masks to prevent the spread of infectious disease.
They vary in shape (rectangular, round) and method of securing (elastic, ties
Note that masks are not respirators. They do not protect you from airborne transmitted diseases, just droplet transmitted disease.

## Slide 6: PPE…. Gadgets
Goggles
Goggles or face shields protect the mucous membranes of the eyes, nose and mouth during situations where blood, body fluid, secretions, or excretions may splash or spray.
Eye glasses do not provide an adequate level of protection.
Goggles cover the top, front and sides of the eye area, providing the proper protection from splashes and sprays that eyeglasses do not. Some brands of goggles can be decontaminated and reused

## Slide 7: PPE Gadgets….Conti
Gloves
It is important to select the right size gloves to provide proper protection from infectious agents. Remember to change gloves if they become torn or heavily contaminated during use. Gloves are not a substitute for hand hygiene!

## Slide 8: PPE ….Gadgets
Respirators
Several types of respirators can be worn to control the spread of infectious disease. Respirators vary in size, shape (oval or round), and level of respiratory protection offered (N95 versus N100).
Unlike masks, respirators must be fit-tested before use to ensure they fit properly. Respirators must have a mask-to-face seal and must be checked annually to make sure they are providing adequate protection. Fit-testing is the procedure used to check for a correct mask-to-face seal and involves testing to ensure there is no air leakage between the mask and the face. Using a respirator that has not been fit-tested for your face provides only droplet based transmission protection, which only reduces the risk of transmission via large particle droplets generated by coughing, sneezing or talking. It will not protect you from airborne transmitted diseases.

## Slide 9: How to Go About it !
Donning PPE
Per CDC guidance, PPE should be donned in the following order:
Gown (or apron/coverall)
Shoe and/or hair covers (if worn)
Mask/respirator
Goggles (or face shield in lieu of mask and goggles)
Gloves (if you are wearing a gown, tuck the gown cuffs securely under each glove)

## Slide 10: To Undo !
Recommended sequence of removal of PPE
Since gloves are considered the most contaminated (compared to masks and gowns) remove first.
The gown can then be removed by handling the portion of the gown that the gloves were on top of (i.e. the most distal portion of the sleeves) as this portion would be considered clean. This is the reason for the order recommended by the CDC.
After removing PPE, discard immediately and properly to prevent contamination of the clean area.
Always remember to perform hand hygiene immediately after removing PPE.

## Slide 11: Removing PPE
Remove PPE in an area where you are not in danger of exposure to the infectious agent, such as a separate room, a porch, a garage, or entryway. Then identify the clean areas and contaminated areas of the PPE.
Clean areas: have not been in contact with infectious agent
Contaminated areas: have been in contact with infectious agent

## Slide 12: Removing PPE
To limit self-contamination, remove PPE in the following order:
1. Gloves
2. Goggles (or face shield)
3. Gown (or apron/coverall)
4. Shoe and/or hair covers (if worn)
5. Mask/ respirator

## Slide 13: Keys to Workplace Safety
Provide supplies for hand hygiene.
All rest rooms must have hot water, soap, and paper towels for proper hand washing.
Hand sanitizer should be available to all visitors and staff; placed at entrances, desks, hallways, staff lounge and waiting areas.

## Slide 14: Post visual alerts
Place signs and posters at the entrances and in strategic places (e.g., restrooms, elevators, cafeterias) to provide staff and visitors with instructions (in appropriate languages) about respiratory hygiene and cough etiquette.

## Slide 15: Provide PPE in the Workplace
Inform staff of the types of PPE that are available in the workplace and where they are located.
PPE should be stored in a secure location, but should be easily accessible by staff when needed.
A policy should be devised to track PPE use, when to replace PPE supply, and how to properly dispose of used PPE