DEPARTMENT  OF  CIVIL ENGINEERING

Semester: Summer 2020					    		    Duration: 7 hours

Subject: Surveying 2			               		       Instructor: Engr. Fawad Ahmad

Q.NO (01)

What is triangulation? Explain the oders of triangulation in detail.

Q.NO (02)

Two triangulation stations A and B, 50 miles apart have elevation 1000 feet and 1100 feet respectively. The intervening ground may be assumed to have uniform elevation of 850 feet. Find the minimum height of signal required at B so that the line of signal may not pass nearer the ground than 15 feet

Q.NO (03)

Explain the direct and indirect methods of contouring in detail.

Q.NO (04)

Explain the different methods for locating soundings.

Q.NO (05)

The scale of the photograph is 1cm = 150m. The photograph size is 30 cm x 30 cm determine the number of photograph required to cover an area of 200 km2, if the longitudinal overlap is 70% and side overlap is 35%