## Slide 1: Embedded Systems
Muhammad Waqas

## Slide 2: 8051
Intel introduced 8051, referred as MCS-51, in 1981
The 8051 is an 8-bit processor
The CPU can work on only 8 bits of data at a time
The 8051 had
  128 bytes of RAM
  4K bytes of on-chip ROM
  Two timers
  One serial port
  Four I/O ports, each 8 bits wide
  6 interrupt sources

## Slide 3
The 8051 became widely popular after allowing other manufactures to make and market any flavor of the 8051, but remaining code-compatible.

## Slide 5
The 8031 is a ROM-less 8051
  Add external ROM to it
  You lose two ports, and leave only 2 ports for I/O operations

## Slide 6
Feature | 8051 | 8052 | 8031 | 
ROM (on-chip program in bytes) | 4K | 8K | 0K | 
RAM (bytes) | 128 | 256 | 128 | 
Timers | 2 | 3 | 2 | 
I/O pins | 32 | 32 | 32 | 
Serial port | 1 | 1 | 1 | 
Interrupt sources | 6 | 8 | 6 | 

## Slide 7
8751 microcontroller
  UV-EPROM
  PROM burner
  UV-EPROM eraser takes 20 min to erase
AT89C51 from Atmel Corporation
  Flash (erase before write)
  ROM burner that supports flash
  A separate eraser is not needed
DS89C4x0 from Dallas Semiconductor, now part of Maxim Corp.
  Flash
  Comes with on-chip loader, loading program to on-chip flash via PC COM port

## Slide 8
DS5000 from Dallas Semiconductor
  NV-RAM (changed one byte at a time), RTC (real-time clock)
  Also comes with on-chip loader
OTP (one-time-programmable) version of 8051
8051 family from Philips
  ADC, DAC, extended I/O, and both OTP and flash

## Slide 9: INSIDE THE 8051 (Registers)
Register are used to store information temporarily, while the information could be
  a byte of data to be processed, or
  an address pointing to the data to be fetched
The vast majority of 8051 register are 8-bit registers
  There is only one data type, 8 bits

## Slide 10
The 8 bits of a register are shown from MSB D7 to the LSB D0
With an 8-bit data type, any data larger than 8 bits must be broken into 8-bit chunks before it is processed

## Slide 11
The most widely used registers
A (Accumulator)
  For all arithmetic and logic instructions
B, R0, R1, R2, R3, R4, R5, R6, R7
DPTR (data pointer), and PC (program counter)

## Slide 14: I/O
The four 8-bit I/O ports P0, P1, P2 and P3 each uses 8 pins
All the ports upon RESET are configured as input, ready to be used as input ports
  When the first 0 is written to a port, it becomes an output
  To reconfigure it as an input, a 1 must be sent to the port
    To use any of these ports as an input port, it must be programmed

## Slide 15
It can be used for input or output, each pin must be connected externally to a 10K ohm pull-up resistor
  This is due to the fact that P0 is an open drain, unlike P1, P2, and P3
  Open drain is a term used for MOS chips in the same way that open collector is used for TTL chips

## Slide 17: WHY PROGRAM 8051 IN C
Compilers produce hex files that is downloaded to ROM of microcontroller
  The size of hex file is the main concern
    Microcontrollers have limited on-chip ROM
    Code space for 8051 is limited to 64K bytes
C programming is less time consuming, but has larger hex file size

## Slide 18
The reasons for writing programs in C
  It is easier and less time consuming to write in C than Assembly
  C is easier to modify and update
  You can use code available in function libraries
  C code is portable to other microcontroller with little of no modification

## Slide 19: Data Types
A good understanding of C data types for 8051 can help programmers to create smaller hex files
Unsigned char
Signed char
Unsigned int
Signed int
Sbit (single bit)
Bit and sfr