Note: Attempt all questions.

Q.NO (01)                                                             		                              (5+5)

- Define the following terms:

- Plastic Equilibrium

- Angular Distortion

- Compressive index

- Ultimate Bearing Capacity

- Poission Ratio of soil.

- A 6m tall cantilever wall retaining the soil that has the following properties:

- C=0

- Ø=30°

- ϒ= 19.2 KN/m3

And the ground surface behind the wall is inclined at a slope of 3 horizontal and 1 vertical. The wall has moved sufficiently to develop active condition. Determine the total normal and shear forces acting on the back of this wall usking Rankine’s Theory.

Q.NO(02)                                                                                                              (5+5)

- What is Bearing Capacity. Also write factors effecting Bearing capacity.

- What is the maximum safe load which can be supported by rectangular footing 2m by 3m with a safety factor of 3. The base of the footing is at 1.6m below the ground surface. The unit weight of soil is 18KN/m3 . The angle of shear resisting Ø=20° (Nc=14.8, Nq=6.4, Nϒ=2.9). Unit cohesion Cu=20 KN/m2. Use Meyerhof analysis.

Q.NO (03)                                                                 		                              (5+5)

- What is settlement. What are its types explian in detail ?

- A soil has compressive index Cc=0.31. At a stress 130KN/m2, the void ratio was 1.02. Calculate

- The void ratio if the stress on the soil is increased to 170KN/m2.

- The total settlement of the stratum of 5m thickness.

********************************Best of Luck***********************************