## Slide 1: Computer Networks
A network is a "group of computers and associated devices that are connected by communication facilities.”
Types of networks:
  Local Area Network (LAN): laboratory/office-scale
  Metropolitan Area Network (MAN): city-scale
  Wide Area Network (WAN): world-wide (Internet -> “collection of networks”)

## Slide 2: Network Topology
STAR
RING
MESH
BUS

## Slide 3: Examples
Ethernet:
  popular, relatively inexpensive, easy-to-install LAN architecture
  uses the CSMA/CD media access control
  data transmission normally occurs at 100 Mbps (10Mbps in the early forms and 10Gbps in the most recent forms)
  partially described in the IEEE 802.3 specification
Wi-Fi:
  popular wireless LAN architecture
  uses a modified version of the CSMA/CA protocol
  partially described in the IEEE 802.11 specification

## Slide 4: ISO/OSI Model
The International Standards Organization (ISO) Open Systems Interconnect (OSI) is a standard set of rules describing the transfer of data between each layer in a network operating system. Each layer has a specific function (i.e., the physical layer deals with the electrical and cable specifications).

## Slide 5: ISO/OSI Model
Physical Layer
  Physical/electrical characteristics
  Cable type, length, connectors, voltage levels, signal durations, ...
  Binary data (bits) as electrical or optical signals.
Data Link Layer
  Defines when/how medium will be accessed for transmission
  Units typically called “frames”; error detection/correction; divided into sublayers, including: MAC = Medium Access Control (MAC address 6f:00:2b:23:1f:32)
Network Layer
  IP = Internet Protocol
  Addressing and routing (IP address 147.94.123.15)

## Slide 6: ISO/OSI Model
Transport Layer
  UDP (User Datagram Protocol)
  TCP (Transmission Control Protocol)
  Addressing (“ports”), error correction, flow control, congestion control
Session Layer
  Management of “sessions”
Presentation Layer
  Data translation, formatting, encryption, compression
Application Layer
  Interface between user applications and lower network services

## Slide 7: What is IP, TCP, UDP?
Internet Protocol (IP):
  Take your message and slap a “header” on it (“packet”)
  What’s in a header?
    Sender address: 112.44.44.23
    Receiver address: 147.12.68.211
    Routers use it to figure out what to do with it (see next slide for routers)
  What does IP do:
    mostly addressing
    used by routers
Data
Header

## Slide 8: Internet + Routers
Router: links parts of a larger network together
Routing using tables:
  “129.74” belongs to University of Notre Dame
  How is the table built?
    Routers talk to each other to exchange what they know about the world (using ICMP = Internet Control Message Protocol)
  Why only remember parts of a network?
    32-bit address consists of network address and computer address
    Class A, B, C networks: 8/16/24 bits for network, rest for computers
      Example: C network 127.45.20.21: 127.45.20 is network address, 21 is computer address (out of 255 computers)
Routing is based on (independent) packets!

## Slide 9: UDP = User Datagram Protocol
Slap on another header
Adds more addressing: “ports”
  IP address tell you which computer
  Ports tell you which application on that computer
  Example: a web server “listens” to requests on port 80
  Web browser: http://www.google.com:80 = http://216.58.216.100:80
    HTTP: HyperText Transfer Protocol
    :80: optional
  Unreliable!
    Packets can get lost; packets can arrive out of order
Data
UDP Header
IP Header
“IP Data”

## Slide 10: TCP = Transmission Control Protocol
Reliable protocol
Adds ports (just like UDP), but also provides:
  In-order delivery of packets (using sequence numbers)
  Reliable delivery: using acknowledgment (ACK) packets
  Flow control:
    control of traffic between sender and receiver
    receiver can throttle sender to avoid getting packets too fast
    explicit: “advertised window” in ACK packet (how many more bytes)
  Congestion control:
    control of traffic flow into the network
    routers can throttle sender to avoid getting too many packets
    implicit: watch ACKs -> missing ACKs = router overload
Packet
ACK

## Slide 11: UDP vs TCP
TCP:
  typical choice of most applications
  do not want to lose data, out-of-order arrival, etc.
  email, web traffic, financial transactions, etc.
UDP:
  can be “faster”
    no flow/congestion control “slowing down” traffic
    no retransmissions
    good for “real-time” traffic
  out-of-order arrival: can also “reorder” at application level
  loss of data: can be acceptable
    missing frames in video/audio stream