## Slide 1: What should be done….
Employee Education
- Develop an “office recycling procedures” packet.
- Send out recycling reminders to all employees including environmental articles.
- Train employees on recycling practices prior to implementing recycling programs.
- Conduct an ongoing training process as new technologies are introduced and new employees join the institution.

## Slide 2: Municipal solid waste disposal methods
Composting
Sanitary landfill
Incineration and pyrolysis
Reuse, recovery and recycle

## Slide 3: COMPOSTING
Aerobic decomposition of organic matter by bacteria and fungi
To ensure a reasonable composting rate following parameters are to be maintained
Temp-25- 50 0 C
pH – 5- 8
Moisture -50 -70%
The material to be composted has to be segregated to remove non bio-degradable materials like glass , plastics ,metals and alloys

## Slide 4: Composting
A proper mix of nutrients like animal waste, sewage sludge is necessary to ensure proper growth of bacteria and fungi
Excess compaction may be avoided
Porous structure should be maintained to ensure free circulation of air
This mixture is arranged in windrows of about 2.5 m width
Turned twice a week

## Slide 5: Composting……
Composting process takes about 4 to 6 weeks
Color of mass becomes dark and organic matter in the solid waste transforms to a stable humus
Continuous aeration and mixing
Composted solid waste is a good nutrient and can be used as a manure after addition of certain conditioners

## Slide 6: Benefits of Composting-
Keeps organic wastes out of landfills.
Provides nutrients to the soil.
Increases beneficial soil organisms (e.g., worms and centipedes).
Suppresses certain plant diseases.
Reduces the need for fertilizers and pesticides.
Protects soils from erosion.
Assists pollution remediation

## Slide 7: Land filling
Features
Careful and scientific site selection
Controlled dumping
Compaction of waste
Provision for collecting leachates

## Slide 8: Land filling…..
Organic wastes are degraded by soil microorganisms
Microbes utilize the oxygen present inside the landfill
Followed by anaerobic decomposition
Water soluble organic compounds generated in this process percolates through the landfill soils

## Slide 9: Land filling….
Land occupied by the land fill becomes unproductive
Insects, rodents, scavenger birds, bad odor are some of the aesthetic problems associated with sanitary landfill
Emission of methane and CO2 and leachate contamination of ground water and soil are the environmental issues connected with sanitary landfill

## Slide 10: Thermal Process
Controlled combustion or conversion by application of heat
Incineration
Organic matter in the solid waste is burnt in excess oxygen to produce gaseous products and a stable incombustible residue
Considerable reduction in the volume of the waste
Land required for the landfill vastly reduced

## Slide 11: Thermal Process…
Residue can be easily and safely disposed
High capital and operation costs, emission of air pollutants
Air pollutants can be removed by scrubbers and electrostatic precipitators
Care should be taken to remove polymeric materials since toxic dioxin is generated during incineration

## Slide 12: Thermal Process…….
Pyrolysis
The combustible organic matter in the solid waste decompose thermally in a pyrolysis reactor kept at a temp of 600- 10000C in an oxygen free environment
The pyrolysis process yields compounds like tar ,oils gaseous phases containing fuel gases like hydrogen ,methane, CO etc.
Solid residue will be carbon and inert materials like glass , metals ,silica etc.
Pyrolysis produces less emissions and produces fuel gas as a byproduct
Chlorine contained polymers also can be handled

## Slide 13: Advantages of thermal process
  Complete destruction of pathogenic bacteria.
  No odor and dust nuisance.
  Cost recovery by selling steam power.
  Can be located near the city so less transportation required.
  Less space for disposal.

## Slide 14: Disadvantages of thermal process
Costly required lot of technical knowledge.
Waste should have high calorific value.
Disposal by dumping in sea.
The bulky and lighter parts don’t settle down.
Emission of gases from incinerator plant creates air pollution problems

## Slide 15: HAZARDOUS WASTE MANAGEMENT
In common hazardous waste treatment facilities, incineration, pyrolysis, detoxification, neutralization can be carried out and the waste is further concentrated stabilized and solidified and ultimately disposed in a secure landfill

## Slide 16: Hazardous waste includes many dangerous substances
Legally, a hazardous waste is any discarded material, liquid or solid, that contains substances known to be:
  fatal to humans or laboratory animals in low doses;
  toxic, carcinogenic, mutagenic, or teratogenic to humans or other life-forms;
  ignitable with a flash point less than 60°C;
  corrosive; or
  explosive or highly reactive (undergoes violent chemical reactions either by itself or when mixed with other materials).

## Slide 17: Federal legislation regulates hazardous waste
Two important federal laws regulate hazardous waste management and disposal in the United States.
  The Resource Conservation and Recovery Act (RCRA, pronounced “rickra”) of 1976.
  The Comprehensive Environmental Response, Compensation, and Liability Act (CERCLA or Superfund Act), passed in 1980 and modified in 1984 by the Superfund Amendments and Reauthorization Act (SARA), is aimed at rapid containment, cleanup, or remediation of abandoned toxic waste sites.
Notes: The Resource Conservation and Recovery Act (RCRA, pronounced “rickra”) of 1976 is a comprehensive
program that requires rigorous testing and management of toxic and hazardous substances. A complex set of rules requires generators, shippers, users, and disposers of these materials to keep meticulous account of everything they handle and what happens to it from generation (cradle) to ultimate disposal (grave) (fig. 13.18).
The Comprehensive Environmental Response, Compensation, and Liability Act (CERCLA or Superfund Act), passed in 1980 and modified in 1984 by the Superfund Amendments and Reauthorization Act (SARA), is aimed at rapid containment, cleanup, or remediation of abandoned toxic waste sites. This statute authorizes the EPA to undertake emergency actions when a threat exists that toxic material will leak into the environment. The EPA is empowered to
bring suit for the recovery of its costs from potentially responsible parties, such as site owners, operators, waste generators, or transporters.
SARA also established (under title III) a community right to know and state emergency response plans that give citizens access to information about what is present in their communities. One of the most useful tools in this respect is the Toxic Release Inventory, which requires 20,000 manufacturing facilities to report annually on releases of more than 300 toxic materials. You can find specific information in the inventory about what is in your
neighborhood. The government does not have to prove that anyone violated a law or what role he or she played in a Superfund site. Rather, liability under CERCLA is “strict, joint, and several,” meaning that anyone associated with a site can be held responsible for the entire cost of cleaning it up, no matter how much of the mess they
made. In some cases property owners have been assessed millions of dollars for removal of wastes left there years earlier by previous owners. This strict liability has been a headache for the real estate and insurance businesses.
17

## Slide 18: Biomedical Waste Management
Biomedical Waste
Waste from hospital, clinics, research laboratories, animal husbandry facilities etc.
Types of wastes
Human anatomical wastes
Animal wastes
Microbiology and biotechnological wastes (cell cultures, toxins, vaccines)
Waste sharps (needles, syringes)
Discarded medicines and drugs
Soiled waste (contaminated with blood and body fluids including cotton dressings)

## Slide 19: Treatment /Disposal methods
Incineration
Deep burial
Secured landfilling
Chemical disinfection
Steam sterilization (Auto calving)
Thermal deactivation
Irradiation and microwave treatment

## Slide 20: Autoclaving
Steam sterilization is also known as autoclaving
The waste is placed in a sealed chamber and exposed to steam at a preset temperature and pressure for a specified time
Processing temp is about 1210C with processing time of around 12 minutes
There is no volume reduction of waste
Generation of offensive odor and toxic emissions are also possible
For large volumes of wastes continuous sterilization units have been developed

## Slide 21: Chemical disinfection
Involves treating the medical wastes with liquid chemical disinfectant
The wastes have to be prepared by grinding them therefore the chemical disinfectant can penetrate and disinfect the entire mass
The particle size, porosity and permeability
Will affect the process of disinfection

## Slide 22: Thermal deactivation
Involves raising the temp to such a level that all infectious agents are destroyed
This process is used mainly in treating liquid wastes which is heated to a preset temperature for a specified period and then is destroyed
Irradiation is a process by which ultraviolet or ionizing radiation is used for destroying infectious diseases. The waste is first shredded and sprayed with water
The mass is then heated with microwave radiation under high temperature

## Slide 23: Disposal Bin System
Have Bio Hazard Label on red, yellow, blue and white bins, Cytotoxic Label on black bin.
Collect the domestic waste (eatables, wrappers, fruit peels, papers etc.) in green bin
Yellow bins needles syringes
Dispose body parts which has been segregated in yellow bin / bag by handing over to Common Biomedical Waste Treatment Facility if available or otherwise Incinerate it.
Don’t dispose infectious waste into black and green bin.
Waste sharps– white container

## Slide 24: E-waste
E-waste management
Reuse--- repairing or upgrading the used electronic equipment
Donate ---- donating reusable electronic equipment's to schools or other non profit organizations
Recycle---- take back programs of electronic goods, heavy metals, plastics, glass etc. can be recycled
Dispose --- disposed in secure landfills ---pretreatment is necessary --- size reduction techniques, like crushing ,grinding or mechanical compaction is used

## Slide 25
        END